## Slide 1: The LHeC Detector Design and its possible marriage with a novel heavy-ion detector at IP2
The LHeC Project
Physics of DIS
Detector [Overview, Components]
Installation Study
Interaction Region
Integration of AA and eh Detectors
Inner Tracker
Dual Collisions at IP2
Remarks on Physics
Summary
Max Klein, University of Liverpool, for the LHeC/FCC-eh Study Group
Presented to ALICE Upgrade meeting, 23.11.2020. special thanks to
Kevin Andre, Nestor Armesto, Oliver Bruening, Andrea Gaddi, Bernhard Holzer, Uta Klein, Peter Kostka, Bruce Mellado, Paul Newman, Ercan Pilicer, Alessandro Polini, Eva Villela, Yuji Yamazaki
Circles in a circle
W Kandinsky

## Slide 2: LHeC – Project, Physics, Parameters

## Slide 3: LHeC, PERLE and FCC-eh
50 x 7000 GeV2: 1.2 TeV ep collider
Operation: 2035+, Cost: O(1) BCHF
CDR: 1206.2913 J.Phys.G (550 citations)
Upgrade to 1034 cm-2s-1, for Higgs, BSM
CERN-ACC-Note-2018-0084 (ESSP)
arXiv:2007.14491, subm J.Phys.G
Powerful ERL for Experiments @ Orsay
CDR: 1705.08783 J.Phys.G
CERN-ACC-Note-2018-0086 (ESSP)
Operation: 2025+, Cost: O(20) MEuro
LHeC ERL Parameters and Configuration
Ie=20mA, 802 MHz SRF, 3 turns 
Ee=500 MeV  first 10 MW ERL facility
BINP, CERN, Daresbury, Jlab, Liverpool, Orsay (IJC), +
60 x 50000 GeV2: 3.5 TeV ep collider
Operation: 2050+, Cost (of ep) O(1-2) BCHF
Concurrent Operation with FCC-hh
FCC CDR:
Eur.Phys.J.ST 228 (2019) 6, 474 Physics
Eur.Phys.J.ST 228 (2019) 4, 755 FCC-hh/eh
Future CERN Colliders: 1810.13022 Bordry+

## Slide 4: Energy Recovery and Synergies
LHeC/FCC-eh: high luminosity, high energy
High ERL power facility P=Ie Ee
This is a programme for high quality SRF (Q0 > 1010),
high current sources, and multiturn to reach high Ee
Future/current ERL developments: distribution of emphasis
- CBETA: high current, single turn - for e cooler (EIC)
- MESA: polarised beam - for new PV asymmetry exp.
- CEBAF: few GeV energy - for study of syn. radiation
- PERLE: high current, multiturn - for exp’s and future
Plans: Daresbury, Darmstadt, Berlin. Revival of KEK ERL
normal conducting ERL machine at BINP
Coordination: Lab Director Group (A Stocchi IJClab for ERL)
European Accelerator R+D Roadmap: CERN council 9/21
ERL Network. ERL workshop series
Technical Synergies of LHeC with other applications
SAPPHIRE: a yy collider : Higgs, eweak and QCD machine
F. Zimmermann et al, arXiv:1208.2827
Racetrack as an injector into FCC-ee [direct into Z]
O. Bruening, Y. Papaphilippou
LHeC-FEL
F. Zimmermann et al, work in progress
Injector into FCC-hh
R. Calaga
Proposal of ERL Version of FCC-ee for high Lumi at high Ee
V Litvinenko, T Roser, M Chamizo-Llatas arXiv: 1909.04437
802 MHz technology: PERLE, FCC-ee, eSPS
F Marhauser, B Rimmer et al
704 MHz SPL Cryomodule (CERN) modified for PERLE
F Gerigk, E Jensen et al.
ALICE (Daresbury) Gun delivered to Orsay for PERLE
D Angal-Kalinin, B Militsyn et al
JLEIC Booster (Jlab) likely to be used in PERLE
F Hannon, B Rimmer et al
Forward Calorimetry: FCC-hh and ee colliders / CALICE..
Inner Tracker/CMOS: ee colliders, new HI detector at IP2
- ….
MK: Slide from October 20

## Slide 5: Published in 2020
arXiv:2007:14491 (400 pages, 300 authors)
5 page summary: ECFA Newsletter Nr 5., August 20
156 Institutions involved
https://cds.cern.ch/record/2729018/files/ECFA-Newsletter-5-Summer2020.pdf

## Slide 6: Physics with Energy Frontier DIS
Raison(s) d’etre of ep/eA
at the energy frontier
Cleanest High Resolution
Microscope: QCD Discovery
Empowering the LHC/FCC
Search Programme
Transformation of LHC/FCChh into
high precision Higgs facility
Discovery (top, H, heavy ν’s..)
Beyond the Standard Model
A Unique
Nuclear Physics Facility
Deep Inelastic Scattering

## Slide 7: Higgs in ep and pp [LHC and FCC]
LH(e)C

## Slide 8: Machine Parameters and Operation - ep
For comparison, HERA I operated at 1031cm-2s-1, and was upgraded by a factor of up to 4 for HERA II
The total luminosity delivered was 1 fb-1 over a running period of 15 years, including shutdowns.
LHeC may operate at 20 x 1000 GeV2 and ”repeat” all of HERA in a short running period.
The initial CDR considers a Ring-Ring ep collider as a back-up solution. May be revived for HE-LHC.
No pileup
arXiv:2007.14401

## Slide 9: Machine Parameters - eA
The LHeC and FCC-eh are the highest energy, most powerful electron-ion colliders the world may build.
Saturation, Parton Dynamics and Structure in Nuclei, Quarkonia, Jets, Tomography of p and Nuclei, ..
arXiv:2007.14401

## Slide 10: LHeC Detector Design and Installation Study

## Slide 11: Kinematics: fwd: in p beam direction, bwd: e direction
bwd
fwd
fwd
bwd
Electrons in bwd direction have low energy (E’e < Ee beam)
in fwd direction high energy up to Ep, Rutherford backscattering
Q2=1 GeV2 is 179o, or eta =4.74 = ln tan theta/2, ~ Ee2 !
Hadrons in bwd direction have low energy Eh < Ee beam
in fwd direction hadrons carry energy up to Ep beam
Asymmetric energy coverage of LHeC detector. Fwd region: resembles hh conditions

## Slide 12: The LHeC Detector Design
arXiv:1206.2913+2007.14491
No pile up, low radiation wrt pp; high precision through overconstrained kinematics: e-h; modular for rapid installation
Tracker radius 40  60cm, B 3.5T; LxD =13 x 9m2 [CMS 21 x 15m2 , ATLAS 45 x 25 m2]..
LHeC Detector Design 7/2020

## Slide 13: title
LHeC Detector in the CDR (1206.2913)

## Slide 14
Bethe Heitler - Luminosity measurement at the LHeC
CDR
1206.2913
JPhysG39
075001(12)
p561-566
LR: photon detector
 acceptance 95%
Luminosity from
BH photons to 1%
BH to another order
… BH(e), QCDC, F2
as cross checks
Forward
Taggers:
See Yuji
Yamazaki
at ICHEP
and in
2007.14491

## Slide 15: 3-beam ep/eA Interaction Region
Synchronous ep/pp operation! Non-interacting p beam to freely pass: aperture
Matching e and p beam sizes (experience from HERA, also for magnet placement)
Head-on collisions 
Dipole magnet before
Hadron Calorimeter

## Slide 16: title
H ten Kate (EP-RD, 16.3.18)
New ideas on
thin magnets
cf. E Perez at
FCC workshop

## Slide 17: LHeC Calorimeters
Complete coverage to +- 5 in (pseudo)rapidity
Central Region: 2012: LAr, 2020 Sci/Fe option.
Forward Region: dense, high energy jets of few TeV
H  bb and other reactions demand resolution of HFS
Backward Region: in DIS only deposits of E < Ee
Barrel Calorimeters
Forward/Backward Calorimeters
arXiv:2007.14491

## Slide 18: The LHeC Detector Design
Inner Tracker
Rapidity to ~5
rO = 60 cm
impact resolution
5-10 µm
40.7 m2 Si

## Slide 19: Installation Study
Detector fits in L3 magnet support
Modular structure
Andrea Gaddi, L Herve et al arXiv:2007.14491
Personal note on
TAKRAF cranes
Tagebau-Ausrüstungen,
KRAne und Förderanlagen
~1983 for L3,
In-kind contribution from
IfH Zeuthen, AdW DDR
Detector Installation
possible within about
two-years shutdown:
pre-mounting on surface

## Slide 20: Integration of eA and AA Detector Concepts

## Slide 21
All Numbers [cm]
1315
e-
p/A
Muon Detector
HCAL-Barrel
FHC-Plug-Fwd
BHC-Plug -Bwd
EMC-Barrel
HCAL-
Endcap-Fwd
HCAL-
Endcap-Bwd
Solenoid
619
154
186
23
23
40
148
FEC-Plug-Fwd
BEC.-Plug-Bwd
548
380
230
170
172
148
Dipole
Dipole
Tracker
Tracker Fwd
Tracker
Bwd
130
p/A
100
Increase of
radii, tracker to 1m,
may reduce B to 1.3T
for same resolution
Overall detector just
fits in L3 support
Rfree(L3)=560 cm
Vertex positions: see below
LHeC detector
with
integrated A3
P.Kostka et al.
Backward calos
then symmetric
with fwd calos
Work in progress

## Slide 22
Overlay ALICE_Tracker - LHeC Detector (in scale)
e-
p/A
p/A
pp/AA vertex at +180cm nominal LHC beam setup

## Slide 23
Possible Arrangement for a combined A3 - LHeC Tracker NOT OPTIMISED
macro pixel - 4layers
strip- 4layers
pixel - 2layers
radius
100 cm
length
294 cm
Various Questions:
- Low or HV CMOS
- Thickness, radiation hardness
(note ep: below 1015cm2n eq.
no pile-up in ep, ..  maybe low)
- Detectors in Vacuum? Elliptic ep pipe 
- Bent wafers?
- Same vertex or 1.87 apart? Cost
- …

## Slide 24: title
P. Kostka – work in progress

## Slide 25: Dual Collisions: AA and eA at IP2

## Slide 26: Optics for IP2
LHC Optics – beta vs path
ALICE
ALICE Luminosity Optics
*=10m
ALICE Luminosity Optics: IP2b=1.87m
Dispersion
Separation bump (std LHC procedure)
Shift in time and vertical xing 140mrad
 No showstopper for ep and AA
B Holzer work in progress

## Slide 27: LHeC IR modified for dual purpose
Detector dipole
Staggered quads
Half-quad (NC)
First of triplet qaudrupoles
Optimisation of synchrotron
radiation (power and Ecrit)
LHeC HERA
E crit keV 270 150
Synrad
Power kW 30 28
For ep/A: synchronous with pp/AA in GPDs and LHCb – keep non-colliding beam apart
with option of pp/AA the non-colliding beam needs to be kept inside pipe:
then: shift transversely (as in regular injection mode) and possibly in time
For pp/AA in IP2: no electron beam in. Collisions at nominal IP (or shifted by 25/4ns)

## Slide 28: Aperture Staggered Quadrupoles
♟
♟
Non-colliding beam

## Slide 29: Aperture Half-Quadrupole
♟
♟
Non-colliding beam

## Slide 30: Q1 and further Quadrupoles
Q2, Q3 desirably NOT Nb3Sn but Nb-Ti as suggested by current experience
B Holzer, S Russenschuck
Aperture of Q1A needs study, when non-colliding p beam is kept in vacuum

## Slide 31: Remarks on Heavy Ion Physics

## Slide 32: title
N. Armesto DIS2018, Kobe, 17.4.18 and E. Ferreiro, LHeC Workshop 2018, Orsay, 28.6.18  2007.14491

## Slide 33: Partons in Nuclei
Direct measurements of R:
Resolution of complete quark and gluon structure (NC+CC)
Disentanglement of nuclear + parton dynamic effects
Deep into saturation region with small strong coupling (pQCD)
LHeC
EIC
Fixed Target
Direct determination of Rg with proton and lead data, full error
arXiv:2007.14491
 FT DIS data limit
Complexity of (de) confinement in proton and nuclei
F.Olness

## Slide 34: title
Joint eA/ep and pp/pA/AA physics in a
common apparatus is probably an ideal
for new heavy ion physics to very high precision.
A common/dual/joint - you name it-
experiment would have unprecedented
reach into physics
AA
from low pT, to quarkonia + hard scales
eA
DIS extended by 3-4 orders of magnitude.
Invites new and further thinking, and to
carefully evaluate gains and drawbacks
of such an enterprise.

## Slide 35: Concluding Remarks

## Slide 36: Three Raisons d’etre of the LHeC
Physics
- Microscope: World’s Cleanest High Resolution
- Empowerment of the LHC Physics Programme
- Creation of a high precision, novel Higgs facility
- Discovery Beyond the Standard Model
- Revolution of Nuclear Particle Physics
Sustainability and Cost
LHC:
- see: SM, Higgs and no BSM
- use: Investment of O(5) BSF
- run: HL LHC until ~2040
LHeC [1206.2913, 2007.14491]
- 1.2 TeV ep/A for O(1)BSF
 Establish novel ep+pp
Twin Collider Facility at CERN:
sustains HL LHC and bridges to
CERN’s long term future
For installation during LS4 (2030+)
and long term use (HE LHC, FCCeh)
Technology
Accelerator: Novel SRF ERL, green power facility
Detector: Novel high tech (CMOS..) apparatus
Keep accelerator and detector base uptodate
while preparing for colliders that cost O(10)BSF

## Slide 37: Questions and Tentative Comments
First derived questions:
Can we generate luminosity at 0 and +1.8m for pp/AA and ep/eA, respectively? yes, time needed sharing
How does our detector change if we integrate A3 into LHeC extension in radius, B reduced, low V CMOS, ..
How would their detector change? Would they profit from the ep detector environment?
Muons, calorimetry? Better answered with A3 insight, one would expect this leads to a hard scale program
How does the physics potential change? eA programme at TeV scales. LHeC is most powerful EIC one can build
Detailed Questions
- Magnetic fields: solenoid: if we go to half our value, and enlarge the radius by 2, we gain factor 2 resolution ok
Dipole: the dipole (and solenoid) would move further out, any problem? Rather not. Note low material magnets
Choice of Silicon technology for IT, are we compatible with them? Probably yes. low V CMOS probably ok for LHeC
Readout and Trigger: speed, data volume, 2 trigger and r/o branches or 1 etc. To be studied
For their design the extended ep beam pipe is a nuisance (as it is for ours) --> place Si inside pipe??? challenging
There are many more..
Initial thoughts and questions: LHeC Meeting 29.10. and tentative answers 23.11.20

## Slide 38
from a UK Document 23.10.20
Following a statement of the LHeC/FCC-eH Advisory Committee, chaired by Herwig Schopper, published in 2007.14491
A first analysis of the merits and opportunities of inegrating the LHeC and “A3” detectors could be interesting to be pursued further.

## Slide 39: backup

## Slide 40: Statement of the IAC to DG, published in 2007.14491
There follows a programme for the coming years which is being established and for us to shape.

## Slide 41: Determination of p and A PDFs at LHeC/FCCeh
N Armesto, FCC Physics Week 1/2018
1509.00792
present
status 
on xg
Pb/p
LHeC: Full error, Δχ2 =1. EPPS Δχ2 =52
gluon
valence
sea

## Slide 42: Physics at LHeC as an EIC

## Slide 43: Heavy Flavour – Strange in ePb - from CC
Max Klein nPDFs with LHeC 10.9.2015 POETIC a PARIS
x=0.05
x=0.00005

## Slide 44: The ERL in more Detail
- LHeC Configuration reduced from 60 to 50 GeV.
- LINAC: 112 cryomodules with 4 cavities each
 Total number of cavities: 896 [ILC: O(104)]
- Configuration may be staged with less RF
- Tunnel is small part of cost and better not
reduced further, synchrotron loss, upgrades..
- ERL reduces power to << GW and dumps at < GeV
 novel, “green” accelerator technology
Positrons: 500pC is 3 109e-/bunch  20mA and 1.2 1017 e-/s
LHeC programme needs e-p predominantly (Higgs) and only
smaller e+p sample, ~fb-1  O(1015) e+/s, still demanding!


## Slide 45: Physics at LHeC as an EIC

## Slide 46: Kinematic Ranges of lA DIS – Past and Future
HERA missed the
electron-ion phase.
No deuterons either.
cf HERA3 in 2001..
Note that LHeC may be
tuned to low energies
√s ≈ 100 GeV instead of
1 TeV – direct overlap
EICs and HERA.
FCC-eh: highest Q2, 1/x
Luminosity: crucial for efficient operation, to access rare channels and high x, and Q2
15 years of HERA luminosity collection may shrink to a few days (ATLAS now up to 1fb-1/day)