## Slide 1: LHeC Detector Design
CDR design 2012
Detector now including FCC-he
Tracker and Calorimeters
Project Development – Next Steps
Max Klein
University of Liverpool
for the LHeC Study Group
Development of the LHeC Detector, DIS17, Brum, 5th of April 2017
For references,
please consult
lhec.web.cern.ch
LHeC CDR
arXiv:1206.2913
J.Phys. G39 (2012) 075001
FCC_eh:
Ee =60 GeV
Ep =50 TeV
HE LHC:
Ep=14 TeV
LHeC:
Ee=60 GeV
Ep= 7 TeV

## Slide 2: titel
Observations
Good angular
coverage but at high x
low Q2
High Q2 to 106
CC at large x > 0.0001
Low Q2 High x
Very fwd hadrons:
High y =0.9  6 GeV
FL “easy”
default energies

## Slide 3: titel
Lower Ep
to access
high x at
lower Q2
Modest
Luminosity
required
 EIC
Lower proton energy

## Slide 4: titel
Ee = 20 GeV
Covers
transition
hadronic
to partonic 
behaviour.
“NO” luminosity
required,
part of FL run
Lower electron energy

## Slide 5: NC Cross Section Correlated Uncertainties (Q2=2 GeV2)
From LHeC CDR

## Slide 6: NC Cross Section Correlated Uncertainties (Q2=20000 GeV2)
From LHeC CDR

## Slide 7: Detector in the CDR
kinematics and requirements
Now: Higgs: maximum fwd acceptance (p direction), better hadronic resolution, crucial
c and b tagging capabilities. Still muon tag only (but muon momentum for FCC-eh for H)

## Slide 8: LHeC Detector in the CDR (2012)
Forward/backward asymmetry in energy deposited and thus in geometry and technology
Present dimensions: LxD =14x9m2 [CMS 21 x 15m2 , ATLAS 45 x 25 m2]
Taggers at -62m (e), 100m (γ,LR), -22.4m (γ,RR), +100m (n), +420m (p)
Tile Calorimeter
LAr electromagnetic calorimeter

## Slide 9: Design Report 2012
CERN Referees
arXiv:1206.2913
600 pages. Physics, Detector and Two Accelerator Options
ring-ring which may be of interest in the HE-LHC context and linac-ring, the default LH(e)C

## Slide 10
CDR authors

## Slide 11: title
LHeC Detector in the CDR (1206.2913)

## Slide 12: Detector Magnets
Dipole (for head on LR) and
solenoid in common cryostat,
perhaps with electromagnetic LAr
3.5T field at ~1m radius to house
a Silicon tracker
Based on ATLAS+CMS experience

## Slide 13: LHeC Detector 2016
PK: Status 11/16

## Slide 14: Dimensions and Multitudes - LHeC

## Slide 15: Installation Study
Detector fits in L3 magnet support
Modular structure

## Slide 16: LHeC Detector

## Slide 17: FCC-eh Detector

## Slide 18: Dimensions and Multitudes – FCC-eh

## Slide 19
LHeC (CDR)
60 GeV * 7 TeV
FCC-he (ERL)
60 GeV * 50 TeV
Interaction Regions for ep with Synchronous pp Operation
Non colliding p beam
Still work in progress:
may not need half
quad if L*(e) < L*(p)
Tentative: εp=2μm, β*=20cm  σp=3μm ≈σe matched! εe=5μm ..
Rogelio Tomas et al

## Slide 20
Detector design: Inner Silicon Tracker (status 3/16)
More detailed designs for other components too. DD4HEP software developments..
An opportunity for R+D and building a novel, challenging 4π detector in the twenties.
Profit from HL LHC detector upgrades, also ILC, with no pileup and small radiation load

## Slide 21: LHeC Silicon Tracker

## Slide 22: The LHeC Silicon Tracker

## Slide 23: LHeC Calorimeters

## Slide 24
FEC
EMC
HAC
HAC/BHC
Cut through Calorimeters at z=510cm
Outer radius: 3.6m

## Slide 25
Software Status
Software based on DD4hep/DDG4 - pre-release software [AIDASoft/DD4hep]; Python, C++
LHeC/FCC detector geometry, material description, R/O description as needed, segmentations and surfaces - ingredients for reconstruction;
DDEve - event display tool for quality judgment and control …
Follow the main developments & build a detector model answering physics questions (reuse of experience and implementations)
Collaboration inside the FCC-Software effort at CERN - information @ http://fccsw.web.cern.ch/fccsw/
Synergies when following closer the FCC-SW initiative - new EDM, geometry/material definitions based of DD4hep as well, using GAUDI for overall steering; aspects of commonly used tracking software (ACTS); fast and detailed simulation ….
Hardware optimisation according to latest R&D (HL-LHC …)

## Slide 26: H bb in LHeC Detector

## Slide 27: Next Steps
Interaction region update
Finish ep Detector software link to Higgs, top, PDF.. physics study
Technology choices for novel, high tech, high precision detector post HL-LHC
CDR for FCC-eh Detector (I/2018)
Update of LHeC Detector Design (IV/2018) – will include cost-energy-physics study
Many thanks to
Andrea Gaddi, Hermann ten Kate, Peter Kostka, Ercan Pilcer,
Brett Parker, Alessandro Polini, Stefan Russenschuck, RogelioTomas and many others

## Slide 28: title

## Slide 29: title