## Slide 1: The LHeC
Project Overview
Physics Programme
Accelerator
Detector
Max Klein, University of Liverpool - University of Geneva, 5.12.2012

## Slide 2: Colliders explored the Fermi Energy Scale
Tevatron to find SUSY and BSM; LEP/SLC to find SUSY and the Higgs; HERA to find Lepto-Quarks
Practical end of HERA xg sensitivity
R.Lopes de Sa (Moriond 11.3.12)
MZ=91.1876±0.0021 GeV (PDG2010)
NNLO!
probable legacy plots/numbers

## Slide 3: What HERA could not do or has not done
HERA in one box
the first ep collider
Ep*Ee=
920*27.6GeV2
√s=2√EeEp=320 GeV
L=1..4 1031cm-2s-1
 ΣL=0.5fb-1
1992-2000 & 2003-2007
Q2= [0.1 -- 3 * 104 ] GeV2
-4-momentum transfer2
x=Q2/(sy) ≅10-4 .. 0.7
Bjorken x
y≅0.005 .. 0.9
inelasticity
Test of the isospin symmetry (u-d) with eD - no deuterons
Investigation of the q-g dynamics in nuclei - no time for eA
Verification of saturation prediction at low x – too low s
Measurement of the strange quark distribution – too low L
Discovery of Higgs in WW fusion in CC – too low cross section
Study of top quark distribution in the proton – too low s
Precise measurement of FL – too short running time left
Resolving d/u question at large Bjorken x – too low L
Determination of gluon distribution at hi/lo x – too small range
High precision measurement of αs – overall not precise enough
Discovering instantons, odderons – don’t know why not
Finding RPV SUSY and/or leptoquarks – may reside higher up
…
The H1 and ZEUS apparatus were basically well suited
The machine had too low luminosity and running time
HEP needs a TeV energy scale machine with 100 times
higher luminosity than HERA to develop DIS physics
further and to complement the physics at the LHC. The
Large Hadron Collider p and A beams offer a unique
opportunity to build a second ep and first eA collider
at the energy frontier [discussed at DIS since Madison 2005]

## Slide 4
60 GeV electron beam energy, L= 1033 cm-2s-1, √s=1.3 TeV: Q2max 106 GeV2, 10-6 < x< 1
Recirculating linac (2 * 1km, 2*60 cavity cryo modules, 3 passes, P < 100 MW, ERL)

## Slide 5: 60 GeV Energy Recovery Linac
CERN 1
CERN 2
Jlab
BNL
Two 10 GeV energy recovery Linacs, 3 returns, 720 MHz cavities

## Slide 6
CERN Referees
Published 600 pages conceptual design report (CDR) written by 200 authors from 60 Institutes and
refereed by 24 world experts on physics, accelerator and detector, which CERN had invited.

## Slide 7
“Critical gravitational collapse”
“BFKL evolution and Saturation in DIS”
5d tiny black holes and perturbative saturation
Talk by A.S.Vera at LHeC Workshop 2008
Circles in a circle
V. Kandinsky, 1923
Philadelphia Museum of Art

## Slide 8: Project Development
2007: Invitation by SPC to ECFA and by (r)ECFA to work out a design concept
2008: First CERN-ECFA Workshop in Divonne (1.-3.9.08)
2009: 2nd CERN-ECFA-NuPECC Workshop at Divonne (1.-3.9.09)
2010: Report to CERN SPC (June)
3rd CERN-ECFA-NuPECC Workshop at Chavannes-de-Bogis (12.-13.11.10)
NuPECC: LHeC on Longe Range Plan for Nuclear Physics (12/10)
2011: Draft CDR (530 pages on Physics, Detector and Accelerator) (5.8.11)
refereed and being updated
2012: Discussion of LHeC at LHC Machine Workshop (Chamonix)
Publication of CDR + 2 Contributions to European Strategy [arXiv]
Chavannes workshop (June14-15, 2012) – CERN: Linac+TDR Mandate
ECFA final endorsement of CDR
http://cern.ch/lhec

## Slide 9
LHC Schedule for the coming decade
as shown by S. Myers at EPS 2011 Grenoble - Principal guidance of CDR [+N years..]

## Slide 10: Detector supported by L3 Magnet
Installation study in CDR (Herve, Ghaddi): 30 months for removal and installation
which is compatible with LHC shutdown for HL-LHC (“LS3”)

## Slide 11: High Precision DIS
High Precision DIS
Q2 >> MZ,W2, hi luminosity, large acceptance
Unprecedented precision in NC and CC
Contact interactions probed to 50 TeV
Scale dependence of sin2θ left and right to LEP
 A renaissance of deep inelastic scattering 
Solving a 40 year puzzle:
αs small in DIS or high with jets?
Per mille measurement accuracy
Testing QCD lattice calculations
Constraining GUT (CMSSM40.2.5)
Charm mass to 3MeV, N3LO

## Slide 12: PDFs from HERA+LHC and LHeC
QCD fit with free
u,d,s, HERA plus ultimate ATLAS and
full systematic error simulation on LHeC
d valence
strange
Direct strange measurement from charged current
Wsc in ep  νcX [high lumi, large range, small spot ~7μm2]
DIS is the appropriate process to determine PDFs (just compare HERA – Tevatron PDF constraints)
LHeC: first time ever to fully determine PDFs, free of symmetry and ad hoc assumptions
in huge and unexplored kinematic range
LHC: precision Drell-Yan data provide constraints
(cf for example the ATLAS determination of s/d)
Yet, high precision (<1%) only achievable at W,Z
scale (miss the evolution) and large eweak-QCD theory uncertainties complicate interpretation

## Slide 13: LHeC and the HL-LHC (SUSY searches)
With high energy and luminosity, the LHC search range will be extended to high masses,
up to 5 TeV in pair production. At correspondingly high x (> 0.5) the PDFs are unknown to
a considerable extent [cf gg luminosity  ğğ and gluon density from LHeC (10% at x=0.6)]
The HL-LHC (search) programme requires a much more precise understanding of QCD,
which the LHeC provides (strong coupling, gluon, valence, factorisation, saturation, diffraction..)

## Slide 14: Higgs and LHeC
Precision measurements of couplings in WW and ZZ production (so far: bb in CC to 4%)
Measurement of CP properties (JPC=0++ in SM; MSSM has 2 CP-even and 1 CP-odd states)
Reduction of theoretical uncertainties for pp measurements
Initial study of WW  H  bb
PGS for detector, cut based analysis,
S/N =1, 500 H-bb events for 100fb-1
With high luminosity the LHeC has a huge potential for precision Higgs physics, which is being further evaluated.
ICHEP12: J Campbell: ultimate limitation of
Higgs measurements from LHC by PDFs/QCD

## Slide 15: Top Quark and Leptoquarks
Leptoquarks (-gluons) are predicted in RPV SUSY,
E6, extended technicolour theories or Pati-Salam.
The LHeC is the appropriate configuration to do their
spectroscopy, should they be discovered at the LHC.
The LHeC is a (single) top quark production
factory, via Wb  t. Top was never observed
in DIS. With ep: top-PDF  6 flavour VFNS,
precision Mt direct and from cross section,
anomalous couplings

## Slide 16: Heavy Ion Physics
unmeasured | known?
up valence
gluon
eA physics is essentially not done yet (no eA at HERA)
LHeC has huge discovery potential for new HI physics
(bb limit, saturation, deconfinement, hadronisation..)
It will put nPDFs on completely new ground and
constrain the initial conditions of the Quark-Gluon Plasma

## Slide 17: Saturation – Low x Physics
New phase of matter: small coupling but
non-linear parton-parton interactions:
End of DGLAP ? BFKL?
Access to 10 TeV scale SUSY via BFKL (“DP”) arXiv:1205.6713 Kowalski, Lipatov, Ross
Restauration of unitarity?
Relevant for UHE neutrino scattering
Precision Measurements of
crucial observables (F2, FL, J/ψ..

## Slide 18
Lev Lipatov in the CDR…
PDFs (t, s, q-q, val, xg)
Odderon
Instanton
(no) saturation, QCD
QGP initial state
Factorization pp-ep
LQs, RPV SUSY
e*
Higgs CP
αs indeed small (GUT)
Candidates for Surprises and Discoveries
Ultra high precision (detector, e-h redundancy) - new insight
Maximum luminosity and much extended range - rare, new effects
Deep relation to (HL-) LHC (precision+range) - complementarity
 LHeC brings a substantial enrichment of LHC physics

## Slide 19: Summary of LHeC Physics [arXiv:1211:4831+5102]

## Slide 20
TOBB ETU
KEK
Accelerator Design: Participating Institutes

## Slide 21: LHeC Parameters
CDR: Two options for electron beam: Ring or (Racetrack) Linac with E-recovery for L > 1033cm-2s-1
Synchronous operation of pp and ep in HL-LHC phase. e Ring required bypassing pp experiments
Source | Power [MW]
Cryogenics (linac) | 21
Linac grid power | 24
SR compensation | 23
Extra RF cryopower | 2
Injector | 6
Arc magnets | 3
Total | 78

## Slide 22
Ring-Ring
Civil engineering studied and reviewed by CH company Amber, both for ring and for linac options. Bypass in
ring option used to house rf. ~4years of installation
Quite some interference with LHC: cryo jumpers (asymmetric FODO), connection of bypasses, access to
LHC, proton dump area (point 3), RF (point 4), .. Cf CDR
June workshop, after CDR: RR not preferred, design LR

## Slide 23: 60 GeV Electron Accelerator
Two 1km long LINACs
connected at CERN territory
Arcs of 1km radius: ~9km tunnel
3 passages with energy recovery
John Osborne (June LHeC Workshop)

## Slide 24: Civil Engineering until 2015
CDR: Evaluation of CE, analysis
of ring and linac by Amber Zurich
with detailed cost estimate
[linac CE: 249,928 kSF..] and time:
3.5 years for underground works using 2 roadheaders and 1 TBM
More studies needed for
Integration with all services
(EL,CV, transport, survey etc).
Geology
Understanding vibration risks
Environmental impact assessment
Tunnel connection in IP2
Shaft sinking installation
Roadheader 1
Roadheader 2
J.Osborne, Chavannes

## Slide 25
from CDR LHeC
Components and Cryogenics
Chapter 9 of CDR
Jlab:
4 1011
Need to develop LHeC cavity (cryo-module)

## Slide 26: CERN Mandate – TDR by ~2015
S.Bertolucci at Chavannes workshop 6/12 based on
CERN directorate’s decision to include LHeC in the MTP

## Slide 27: RF Development
Frequency choice: n * 120.237 MHz
N=6: 721 MHz, n=11: 1.3GHz (XFEL)
SPL cryomodule 704 MHz
BNL 704 MHz cavity (20 MV/m with
high Q0 demonstrated)
Detailed comparison (threshold current, cryo power,
Rf power, size, cost, collaboration, synergy..)
ALICE 1.3 GHz, not CW – only EU ERL facility operational
Daresbury develops cryomodule for ESS (700 MHz)
CERN: in house collaboration with SPL, and eRHIC/BNL
Accelerator physics motivation:
  ERL demonstration, FEL, γ-ray source, e-cooling demo!
  Ultra-short electron bunches
One of the 1st low-frequency, multi-pass SC-ERL
  synergy with SPL/ESS and BNL activities
High energies (200 … 400 MeV) & CW
Multi-cavity cryomodule layout – validation and gymnastics
Two-Linac layout (similar to LHeC)
MW class power coupler tests in non-ER mode
Complete HOM characterization and instability studies!
Cryogenics & instrumentation test bed … E.Jensen
Steps: Design of LHeC ERL TF, cavity-cryo module (hi Q),
lattice, optics, magnets, source, ….
Watch out for surprises as humming bird:
Building international collaboration
(CERN,Daresbury, Jlab, others?)
beam structure at ALICE with 230-kV DC gun voltage

## Slide 28: LHeC - ERL-TF
5 MeV
DE = 75 MeV
DE = 75 MeV
5 MeV
DC = l/2
7.07065
0
10
0
2
-2
BETA_X&Y[m]
DISP_X&Y[m]
BETA_X
BETA_Y
DISP_X
DISP_Y
Tentative study of multipass optics and lattice
Arc 3 - 230 MeV optics
Development of LHeC Testfacility at CERN in international collaboration (ASTeC, Jlab, +)

## Slide 29: Magnets Developments
flux density in the gaps | 0.264 T 0.176 T 0.088 T
magnetic length | 4.0 m
vertical aperture | 25 mm
pole width | 85 mm
number of magnets | 584
current | 1750 A
number of turns per aperture | 1 / 2 / 3
current density | 0.7 A/mm2
conductor material | copper
resistance | 0.36 m
power | 1.1 kW
total power 20 / 40 / 60 GeV | 642 kW
cooling | air
LR recirculator dipoles and quadrupoles
New requirements (aperture, field)?
Combined apertures?
Combined functions (for example, dipole + quad)?
LR linac quadrupoles and correctors
New requirements (aperture, field)?
More compact magnets, maybe with at least two
families for quadrupoles?
Permanent magnets / superconducting for quads?
A.Milanese, Chavannes workshop
Prototypes for Ring dipoles
Fabricated and tested by
CERN (top) and Novosibirsk
1/2m dipole model
Full scale prototype
Quadrupole for Linac
Magnets for ERL test stand
Collaboration of CERN, Daresbury and Budker (Novosibirsk)

## Slide 30: Interaction Region Developments
Have optics compatible with LHC and β*=0.1m
Head-on collisions mandatory 
High synchrotron radiation load, dipole in detector
Specification of Q1 – NbTi prototype ( with KEK?)
Revisit SR (direct and backscattered),
Masks+collimators
Beam-beam dynamics and 3 beam operation studies
Optimisation: HL-LHC uses IR2 quads to squeeze IR1
(“ATS” achromatic telescopic squeeze) Start in IR3.? R.Tomas et al.
Beam pipe: in CDR 6m, Be, ANSYS calculations
Composite material R+D, prototype, support..
 Essential for tracking, acceptance and Higgs

## Slide 31: LHeC Detector Overview
Forward/backward asymmetry in energy deposited and thus in geometry and technology
Present dimensions: LxD =14x9m2 [CMS 21 x 15m2 , ATLAS 45 x 25 m2]
Taggers at -62m (e),100m (γ,LR), -22.4m (γ,RR), +100m (n), +420m (p)
Tile Calorimeter
LAr electromagnetic calorimeter
Detector option 1 for LR and full acceptance coverage

## Slide 32: Detector Magnets
Dipole (for head on LR) and
solenoid in common cryostat,
perhaps with electromagnetic LAr
3.5T field at ~1m radius to house
a Silicon tracker
Based on ATLAS+CMS experience

## Slide 33: Silicon Tracker and EM Calorimeter
Transverse momentum
Δpt/p2t  6 10-4 GeV-1
transverse
impact parameter
 10μm
LHeC-LHC: no pile-up, less radiation, smaller momenta apart from forward region

## Slide 34: Liquid Argon Electromagnetic Calorimeter
Inside Coil
H1, ATLAS
experience.
Barrel: Pb, 20 X0 , 11m3
fwd/bwd inserts:
FEC: Si -W, 30 X0 ,0.3m3
BEC: Si -Pb, 25 X0,0.3m3
GEANT4 Simulation

## Slide 35: Hadronic Tile Calorimeter
Outside Coil: flux return
Modular. ATLAS experience.
Combined GEANT4 Calorimeter Simulation
+5.9m
-3.6m
R=2.6m

## Slide 37
The LHeC is an upgrade of the LHC, to operate with it, and not the next world project

## Slide 38: Summary
The LHeC has a unique physics programme (QCD, Higgs, BSM, HI).
It has a rich synergy with the LHC, SPL,ESS.. and links NP and PP.
The now published design report moved the dream of a TeV scale
electron-hadron collider to the “real axis” (SB). It can be done. The
LHeC is the only new collider for CERN which can live with the LHC.
Many thanks to CERN, NuPECC, ECFA and to the expanding LHeC Group
“Energy frontier,
Precision,
QCD,
QGP”
Tatsuya Nakada
Cracow 9/12 ESG

## Slide 39: Backup slides

## Slide 40: ATLAS Higgs projections
Updated in October 2012

## Slide 41: Precision Measurements

## Slide 42: linac e+ source options
recycle e+ together with energy, multiple use,
  damping ring in SPS tunnel w t~2 ms
Compton ring, Compton ERL, coherent pair production, or undulator for high-energy beam
3-ring transformer & cooling scheme
accumulator ring (N turns)
fast cooling ring (N turns)
extraction ring (N turns)
(Y. Papaphilippou)
(E. Bulyak)
(H. Braun,
E. Bulyak,
T. Omori,
V. Yakimenko)
(D. Schulte)

## Slide 43: ERL Test Facilities
BNL 704 MHz cavity (20 MV/m with
high Q0 demonstrated)
IHEP ERL-TF | HZB BERLinPro | BINP | Peking FEL | BNL ERL-TF | KEK cERL | Daresbury ALICE | JAERI | CERN ERL-TF
35 MeV | 100 MeV | 11-40 MeV | 30 MeV | 20 MeV | 245 MeV | 10 MeV | 17 MeV | 300 MeV
1.3 GHz 9 cell | 1.3 GHz | 180 MHz | 1.3 GHz 9-cell | 704 MHz 5-cell | 1.3 GHz 9-cell | 1.3 GHz 9-cell | 500 MHz | 721 MHz 2x4x5 cell
10 mA | 100 mA | 30 mA | 50 mA | 50-500 mA | 10-100 mA | 13 µA | 5-40 mA | 2-6 mA
60 pC | 10-77 pC | 0.9-2.2 nC | 60 pC | 0.5-5 nC | 77 pC | 80 pC | 400 pC | 500 pC
1 pass | 1-2 pass | 4 passes | 1 pass | 1 pass | 2 passes | 1 pass | 1 pass | 2 passes
under construction | planned / construction | operating |  | under construction | under construction | operating | operating | first ideas
E.Jensen

## Slide 44: CDR - Time Schedule*)
LHeC is to operate synchronous with HL-LHC
LS3 requires 2-3 years for ATLAS+. It is the
one extended time period, which will allow
installation and connection of LHeC
Detector installation
study for IP2, reuse
of L3 magnet as
support for LHeC.
Estimated 30 months
*) LS3  schedule most likely shifted by +2 years

## Slide 45: In-medium Hadronisation
The study of particle production in eA (fragmentation functions and hadrochemistry)
allows the study of the space-time picture of hadronisation (the final phase of QGP).
Low energy (): need of
hadronization inside.
Parton propagation: pt broadening
Hadron formation: attenuation
High energy (): partonic
evolution altered in the
nuclear medium.
LHeC :
+ study the transition from small to high energies in much extended range wrt. fixed target data
+ testing the energy loss mechanism crucial for understanding of the medium produced in HIC
+ detailed study of heavy quark hadronisation …
W.Brooks, Divonne09
Notes: 45

## Slide 46: LR LHeC IR layout & SC IR quadrupoles
Non-colliding proton beam
colliding proton beam
Electron beam
Synchrotron radiation
High-gradient SC IR quadrupoles based on Nb3Sn for colliding proton beam with common low-field
Inner triplets
Exit hole for electrons & non-colliding protons
Inner triplets
Q1
Q2
Q2
Q1
Nb3Sn (HFM46): 5700 A, 175 T/m, 4.7 T at 82% on LL (4 layers), 4.2 K | Nb3Sn (HFM46): 8600 A, 311 T/m, at 83% LL, 4.2 K
46 mm (half) ap., 63 mm beam sep. | 23 mm ap.. 87 mm beam sep.
0.5 T, 25 T/m | 0.09 T, 9 T/m
As shown by F. Zimmermann at Chamonix12

## Slide 47
About 180 Experimentalists and Theorists from 60 Institutes
Tentative list of those who contributed to the CDR
Supported by
CERN, ECFA, NuPECC
http://cern.ch/lhec

## Slide 48: UK Accelerator Engagement
Topics of joint interest and priority
Meeting ASTEC/CI 5.9.12 at CERN
Electron source for TF
Design of IR, Optics for p beams, synrad tracking
Test facility design (OPAC fellow)
Sc cavity design, coupler, HOM damper, tuner..
Instrumentation for TF…
With only somewhat reduced priority: beam dynamics,
positron source, magnets ..
Preparation of MoU, with view also to other partners
Deepa Angal-Kalinin1, Robert Appleby5, Ian Bailey3, Steve Buckley1, Graeme Burt3, Neil Bliss2, Swapan Chattopadhyay3,4,5, Jim Clarke1, Peter Corlett1, Philippe Goudket1, Andy Goulden1, Joe Herbert1, Kai Hock4, Frank Jackson1, Steve Jamison1, James Jones1, Lee Jones1, Alexander Kalinin1, Oleg Malyshev1, Neil Marks1, Peter McIntosh1, Julian McKenzie1, Keith Middleman1, Boris Militsyn1, Andy Moss1, Bruno Muratori1, David Newton4, Tim Noakes1, Shrikant Pattalwar1, Yuri Saveliev1, Ben Shepherd1, Susan Smith1, Rob Smith1, Trina Thakker1, Luke Thompson5, Reza Valizadeh1, Carsten Welsch4, Alan Wheelhouse1, Peter Williams1, Andy Wolski4
1ASTeC/STFC, 2TD/STFC, 3University of Lancaster, 4University of Liverpool, 5University of Manchester
The LHeC represents a unique opportunity
for the Daresbury Campus (ASTEC and CI),
but also for the wider UK accelerator
community (A.Seryi co-author of CDR) to be
at the forefront of accelerator developments,
building on their unique expertise, a very
welcome strong expression of interest, and its
strong links to Universities, CERN and industry.

## Slide 49: ATLAS and LHeC Silicon Trackers
 New ATLAS Si tracker
LHeC forward (LHCb link!) and backward telescopes and central Si
LHeC: no pile-up, less radiation, smaller momenta apart from forward region
Tentative designs as of 2012