gndmap

This is an outline of an alternative proposal for the grounding and shielding of the SCT barrel and forward detectors

Tony Smith Feb ‘00

The main differences to the original scheme are

Module grounds are tied directly to the support structure and cooling tubes with the aim of minimising the impedance between any two modules in order to minimise voltage differences between any two modules or between modules and the support structure.