VELO hardware interlocks implementation

Tony Smith, Ann Van Lysebetten xxxxx

V1.1 15/04/2008

- Introduction

The VELO hardware interlock system has been developed to protect the VELO against all kinds of failures during operation. The functionality of the system is described in details in reference [1]. This document presents the follow-up to the functionality description.

Table 1 gives the overview of all the interlock signals for the VELO as described in reference [1]. The first group of interlock signals is taken via the interlock glue box. Details are given in section 2. The second group of signals is exchanged directly between the PLCs. Section 3 gives an overview of the implementation. The VELO relies on a few external signals for the interlocks. These are shown in group 3 of table 1. Details are given in section 4.

Table 1: Overview of the hardware interlocks for the VELO

| Signal | From system | To system | Granularity |
| --- | --- | --- | --- |
| LV inhibit | Front-end | LV | per LV module |
| LV inhibit | Cooling | LV | per detector half |
| LV inhibit | Vacuum | LV | full system |
| Temp Board Off | Front-end | LV | per LV module |
| HV inhibit | Vacuum | HV | full system |
| HV inhibit | Cooling | HV | per detector half |
| HV inhibit | Front-end | HV | per ½ HV module |
| Temp Board Off | Front-end | HV | per ½ HV module |
| BCM off | LHCb BCM | HV | full system |
| BCM off | LHCb BCM | Positioning | full system |
| Cooling inhibit | Front-end | Cooling | per detector half |
| Temperature Board ready | Front-End | Cooling | per detector half |
| Cooling inhibit | Vacuum | Cooling | full system |
| Positioning inhibit | Vacuum | Positioning | full system |
| Venting inhibit | Cooling | Vacuum | full system |
| Vent/evacuate inhibit | Positioning | Vacuum | full system |
| Cooling inhibit | Primary water | Cooling | full system |
| Positioning inhibit | LHCb BAS | Positioning | full system |
| Beam inhibit | Positioning | LHCb BAS |  |
| Vent/evacuate inhibit | LHC vacuum | Vacuum | full system |
| Gas ready | Gas injection | Vacuum | full system |

- The interlock glue box

  - Description of the incoming signals

The granularity consists of 2 VELO modules; this is dictated by the granularity of the too warm signal from the temperature board. For a too warm signal 1 LV module and a ½ HV module will be switched off. Details on the temperature board can be found in reference [2]. The temperature board triggers 3 types of signals that are sent to the interlock box:

- “too cold”: one signal per board, or 3 per detector half. The signal is triggered when the temperature given by 3 out of 32 NTCs (per temperature board) on the VELO modules is below -40(C.

- “too warm”: 4 signals per board, 1 signal per 2VELO modules. The signal is triggered when one of the NTCs on the VELO modules reads a temperature greater than 30 (C.

- Temperature board ok: The signal is high (ok) when the boards are powered. One signal per board is given.

Masking of the signals via PVSS can be done. However this is not automatic, a special file needs to be loaded. Accidental masking of crucial parameters will generate an automatic interlock signal:

- If 4 NTCs on one module are masked the interlock is fired

- Errors masked interlock fired

Other incoming signals are from the cooling system, BCM and vacuum system.

- Cooling system signals that the cooling has enough cooling power

  - This is defined as …..

- Vacuum system delivers a vacuum ok signal

  - This is defined as ….

- From the BCM a signal that the BCM is on is given.

Table 2 gives an overview of these signals as seen by the interlock box. Each temperature board has its own input signals.

| Input signal | No of signals | From | Signal |
| --- | --- | --- | --- |
| Warm ok 0/1/2/3 | 4 per TB | Temp. Board | Too warm |
| Cold ok | 1 per TB | Temp. Board | Too cold |
| Board ok | 1 per TB | Temp. Board | Temp board ok |
| Cooling ready A/C | 1 per det half | Cooling |  |
| Vacuum ready | 1 | Vacuum |  |
| BCM ok | 1 | BCM |  |

  - Description of the outgoing signals

The output signals to HV and LV are divided according to the granularity of the temperature boards. Spare channels exist.

Table 3 gives an overview of the outgoing signals.

| Output signal | No of signals | To |
| --- | --- | --- |
| CAEN01-11 | 12 | LV |
| A/C_ISEG01/02/03 | 12 | HV |
| Allow CoolingA/C | 2 | Cooling |
| Allow positioning | 1 | Motion |

2.1 Description of the interlock glue box

All the incoming and outgoing signals have 2 LEDs on the front panel. If the green LED is on the signal is correctly coming in or going out. If this is not the case for outgoing signals the interlock is fired. For incoming signals the signal is absent. Next to the green LED an orange LED can be seen. If this one is lit it means that the signal has been forced from the inside. The forcing is done by the override switches inside the box (see document xxx).

2.1.1 Programming of the FPGA

The FPGA in the interlock box takes the input signals and fires the right output signals taking into account the granularity as described in table . The programming logic follows the signal firing as described in table 1. Below a short overview is given:

  - Temperature board fires “too warm” (warm ok led goes off)

    - CAEN01-11 leds on front panel will go off and switch off of corresponding LV modules (LV inhibit)

    - A/C_ISEG01/02/03 leds go off and switch off corresponding HV modules (HV inhibit)

  - Temp board fires too cold (cold ok led goes off):

    - Allow cooling A/C led will go off and cooling system will go to BU cooling.

    - Note that the information of the Temperature boards (too cold signal) is ignored by the cooling system when the TB looses the temp board ok signal.

  - Temp board fires not ok (temp ok led off)

    - CAEN01-11 leds on front panel will go off and switch off of corresponding LV modules (LV inhibit)

    - A/C_ISEG01/02/03 leds go off and switch off corresponding HV modules (HV inhibit)

    - too cold signal is ignored by the cooling system.

  - Vacuum not read y (vacuum ready ok les goes off)

    - CAEN01-11 leds on front panel will go off and switch off of corresponding LV modules (LV inhibit)

    - A/C_ISEG01/02/03 leds go off and switch off corresponding HV modules (HV inhibit)

  - Cooling not ready (cooling ok A/C led goes off)

    - CAEN01-11 leds on front panel will go off and switch off of corresponding LV modules (LV inhibit)

    - A/C_ISEG01/02/03 leds go off and switch off corresponding HV modules (HV inhibit)

  - BCM not ok (BCM ok goes off)

    - A/C_ISEG01/02/03 leds go off and switch off corresponding HV modules (HV inhibit)

    - Allow positioning goes off, detector will retract and is not allowed to move in.

2.2 testing the glue box

To test all input and output signals a check list was made.  An example of this checklist can be found in appendix A.

- Signals exchanged between the PLCs

  - Cooling-vacuum system

- Cooling inhibit

- Venting inhibit

  - Vacuum system – motion

- Positioning inhibit

- External Signals

  - Signal exchange with the LHC vacuum

  - DSS signal

A DSS signal is sent to the cooling PLC when the temperature or flow of the primary cooling water is not ok [3]. In this case the cooling will switch to backup cooling. The status of this signal can be seen in the interlock panel on the cooling PLC (see also reference [4]).

  - Signal exchange for the beam dump

References

[1] Velo Hardware interlocks, EDMS document 706629 v2.0

[2] temperature board

[3] DSS document

[4] Cooling manual

APPENDIX A

Interlock box test check list: Check done on ………………..….   By …………………….

| Side | Origin | Signal input | Cable in | In LED ok? | Signal output | Cable out | Out LED ok? | Action ok? | remark |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A | TB1 | Cold ok |  |  | Allow Cooling A |  |  |  |  |
|  | TB2 | Cold ok |  |  | Allow Cooling A |  |  |  |  |
|  | TB3 | Cold ok |  |  | Allow Cooling A |  |  |  |  |
|  | TB1 | Warm ok 0 |  |  | A_ISEG01 0-3 | A_ISEG 01 low |  |  |  |
|  |  | Warm ok 0 |  |  | CAEN 11 |  |  |  |  |
|  | TB1 | Warm ok 1 |  |  | A_ISEG01 4-7 | A_ISEG 01 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 01 |  |  |  |  |
|  | TB1 | Warm ok 2 |  |  | A_ISEG01 8-11 | A_ISEG 01 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 02 |  |  |  |  |
|  | TB1 | Warm ok 3 |  |  | A_ISEG01 12-15 | A_ISEG 01 up |  |  |  |
|  |  | Warm ok 3 |  |  | CAEN 03 |  |  |  |  |
|  | TB2 | Warm ok 0 |  |  | A_ISEG02 0-3 | A_ISEG 02 low |  |  |  |
|  |  | Warm ok 0 |  |  | CAEN 04 |  |  |  |  |
|  | TB2 | Warm ok 1 |  |  | A_ISEG02 4-7 | A_ISEG 02 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 05 |  |  |  |  |
|  | TB2 | Warm ok 2 |  |  | A_ISEG02 8-11 | A_ISEG 02 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 06 |  |  |  |  |
|  | TB2 | Warm ok 3 |  |  | A_ISEG02 12-15 | A_ISEG 02 up |  |  |  |
|  |  | Warm ok 3 |  |  | CAEN 07 |  |  |  |  |
|  | TB3 | Warm ok 0 |  |  | A_ISEG03 0-3 | A_ISEG 03 low |  |  |  |
|  |  | Warm ok 0 |  |  | CAEN 08 |  |  |  |  |
|  | TB3 | Warm ok 1 |  |  | A_ISEG03 4-7 | A_ISEG 03 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 09 |  |  |  |  |
|  | TB3 | Warm ok 2 |  |  | A_ISEG03 8-11 | A_ISEG 03 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 10 |  |  |  |  |
|  | TB3 | Spare |  |  | A_ISEG03 12-15 (spare) | A_ISEG 03 up |  |  |  |
|  |  | Spare |  |  | CAEN spare |  |  |  |  |
|  | TB1 | Board ok |  |  | A_ISEG01 0-15 | A_ISEG 01 up/low |  |  |  |
|  |  |  |  |  | CAEN 11-03 |  |  |  |  |
| Side | Origin | Signal input | Cable in | In LED ok? | Signal output | Cable out | Out LED ok? | Action ok? | remark |
|  | TB2 | Board ok |  |  | A_ISEG02 0-15 | A_ISEG 02 up/low |  |  |  |
|  |  |  |  |  | CAEN 04-07 |  |  |  |  |
|  | TB3 | Board ok |  |  | A_ISEG03 0-15 | A_ISEG 03 up/low |  |  |  |
|  |  |  |  |  | CAEN 08-10 + spare |  |  |  |  |
|  | TB1 | Board ok + Cold ok |  |  | Allow Cooling A |  |  |  |  |
|  | TB2 | Board ok + Cold ok |  |  | Allow Cooling A |  |  |  |  |
|  | TB3 | Board ok + Cold ok |  |  | Allow Cooling A |  |  |  |  |
| C | TB1 | Cold ok |  |  | Allow Cooling C |  |  |  |  |
|  | TB2 | Cold ok |  |  | Allow Cooling C |  |  |  |  |
|  | TB3 | Cold ok |  |  | Allow Cooling C |  |  |  |  |
|  | TB1 | Warm ok 0 |  |  | C_ISEG01 0-3 | C_ISEG 01 low |  |  |  |
|  |  | Warm ok 0 |  |  | CAEN 11 |  |  |  |  |
|  | TB1 | Warm ok 1 |  |  | C_ISEG01 4-7 | C_ISEG 01 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 01 |  |  |  |  |
|  | TB1 | Warm ok 2 |  |  | C_ISEG01 8-11 | C_ISEG 01 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 02 |  |  |  |  |
|  | TB1 | Warm ok 3 |  |  | C_ISEG01 12-15 | C_ISEG 01 up |  |  |  |
|  |  | Warm ok 3 |  |  | CAEN 03 |  |  |  |  |
|  | TB2 | Warm ok 0 |  |  | C_ISEG02 0-3 | C_ISEG 02 low |  |  |  |
|  |  | Warm ok 0 |  |  | CAEN 04 |  |  |  |  |
|  | TB2 | Warm ok 1 |  |  | C_ISEG02 4-7 | C_ISEG 02 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 05 |  |  |  |  |
|  | TB2 | Warm ok 2 |  |  | C_ISEG02 8-11 | C_ISEG 02 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 06 |  |  |  |  |
|  | TB2 | Warm ok 3 |  |  | C_ISEG02 12-15 | C_ISEG 02 up |  |  |  |
|  |  | Warm ok 3 |  |  | CAEN 07 |  |  |  |  |
|  | TB3 | Warm ok 0 |  |  | C_ISEG03 0-3 | C_ISEG 03 low |  |  |  |
| Side | Origin | Signal input | Cable in | In LED ok? | Signal output | Cable out | Out LED ok? | Action ok? | remark |
|  |  | Warm ok 0 |  |  | CAEN 08 |  |  |  |  |
|  | TB3 | Warm ok 1 |  |  | C_ISEG03 4-7 | C_ISEG 03 low |  |  |  |
|  |  | Warm ok 1 |  |  | CAEN 09 |  |  |  |  |
|  | TB3 | Warm ok 2 |  |  | C_ISEG03 8-11 | C_ISEG 03 up |  |  |  |
|  |  | Warm ok 2 |  |  | CAEN 10 |  |  |  |  |
|  | TB3 | Spare |  |  | C_ISEG03 12-15 (spare) | C_ISEG 03 up |  |  |  |
|  |  | Spare |  |  | CAEN spare |  |  |  |  |
|  | TB1 | Board ok |  |  | C_ISEG01 0-15 | C_ISEG 01 up/low |  |  |  |
|  |  |  |  |  | CAEN 11-03 |  |  |  |  |
|  | TB2 | Board ok |  |  | C_ISEG02 0-15 | C_ISEG 02 up/low |  |  |  |
|  |  |  |  |  | CAEN 04-07 |  |  |  |  |
|  | TB3 | Board ok |  |  | C_ISEG03 0-15 | C_ISEG 03 up/low |  |  |  |
|  |  |  |  |  | CAEN 08-10 + spare |  |  |  |  |
|  | TB1 | Board ok + Cold ok |  |  | Allow Cooling C |  |  |  |  |
|  | TB2 | Board ok + Cold ok |  |  | Allow Cooling C |  |  |  |  |
|  | TB3 | Board ok + Cold ok |  |  | Allow Cooling C |  |  |  |  |
| A | Cool. PLC | Cooling ready A |  |  | A_ISEG01-02-03 | A_ISEG 01-03 up-low |  |  |  |
|  |  |  |  |  | A_CAEN 0-11 |  |  |  |  |
| C |  | Cooling ready C |  |  | C_ISEG01-02-03 | C_ISEG 01-03 up-low |  |  |  |
|  |  |  |  |  | C_CAEN 0-11 |  |  |  |  |
| A/C | Vac. PLC | Vacuum ready |  |  | A_ISEG01-02-03 C_ISEG01-02-03 | A_ISEG 01-03 up-low C_ISEG 01-03 up-low |  |  |  |
|  |  |  |  |  | A_CAEN 0-11 C_CAEN 0-11 |  |  |  |  |
| A/C | BCM | BCM ok |  |  | Allow close |  |  |  |  |
|  |  |  |  |  | A_ISEG01-02-03 C_ISEG01-02-03 | A_ISEG 01-03 up-low C_ISEG 01-03 up-low |  |  |  |