# B4cables description

This layout is for a pair of  flexible cables made from 3 copper layers with 75um kapton between each layer.

Surface mounted connectors are mounted on the back side.

A solder resist is required on both sides.

Stiffeners of 500um FR4 are required at each connector area.