# K4 Hybrid population notes

Circuits are identical on both sides.

These boards have 16 silicon die wire bonding sites on each side. Capacitors C1 – C32 and even numbered capacitor arrays are very close to these bond pads and the pads must be masked to avoid solder splashes. The masking material must be completely removed after soldering.

Components per side:

C1-115

--- C1 - C32     	32 off 	0.1uf 10V X7R 0603

--- C31 - C63    	31 off 	2.2uF 10V X7R 1206

--- C64        			does not exist

--- C65 - C79 			not loaded

--- C80 				does not exist

--- C81 – C113			not loaded

--- C114 - C115  	 2 off 	10nF 500V X7R 1206

---CX1-32 		32 off 	capacitor array  4 * 0.1uf X7R 10V  0603

R1-35

--- R1-R2    			not loaded

--- R3- R4        	2 off     100R    0603

----R5-R6    			not loaded

--- R7 - R10		4 off      75R    0603

--- R11- R16 			not loaded

--- R17 - R18, R23	3 off   zero ohms 0603

--- R19 - R22    		4 off     2K49    0603

--- R24 - R27			not loaded

--- R28, R30, R32   	3 off      50R    0603

--- R29, R31, R33-R35 	not loaded

SENS1			 not loaded

SK11      	140 pin AMP connector 177983-6 receptacle

SK13		140 pin AMP connector 177983-6 receptacle (pins removed)

***** IMPORTANT ****** Notes on connectors. The holes in the circuit for the connector location pins are too big and will allow incorrect orientation and misalignment.

Please take care to:

1) Ensure correct orientation, It is obvious which way round the connector with the pins removed (sk13) fits. The fully pinned connector is mounted the same way round (check the tabs at each end of the connectors).

2) Centralize the connector pins with the pads in both the long and the short axes of the connector, solder one pin at one end and check the alignment. If OK then solder a pin at the other end and check again. Adjust as necessary and then solder all pins.