# Velo hybrid Version 1

Tony Smith

Liverpool University

# Hybrid

- 4 layer 15 um copper,  50/100 um Kapton

- 500 um carbon fibre base (insulated)

- 100um minimum track and gap

- ~ 1500  * 500 um pads 200 um holes

- 2 trace layers

- starred segmented ground plane

- wide solid power stripe

- guarded HT line & 3 stage filter

- 2 * 100 pin  0.8mm pitch connectors

- 2 reference / tooling holes for assy

- grounding connections on each edge

Test cables

- 2 cables, one power and signals, one signals only

- double sided 18 um copper 100 um Kapton

- 100 ohm differential LVDS input lines

- 50 ohm single ended CMOS I/O

- 75 ohm single ended analog outputs

- wide power and ground

- 300 mm long – can be daisy chained

Adapter PCB

- Standard FR4 double sided pcb

- converts 2 * 100pin connectors to

4 * 50pin Cannon connectors

- compatible with  Vaccum feedthroughs

- use female Cannon for feedthroughs

- use male Cannon directly to support card