## Slide 1: GCT: progress since Liverpool meeting
Introduction
Installation of CHEC-M on prototype telescope
GCT First Light
Inauguration of GCT
Progress with structure
CHEC-M studies
CHEC-S mechanical design
Electronics for CHEC-S
Pre-production GCTs
Summary
Tim Greenshaw, Liverpool University, for GCT group
Notes: The Cherenkov Telescope Array (CTA) is the next generation observatory for ground-based gamma-ray astronomy. Current instruments (HESS, MAGIC and VERITAS) have made huge progress in the observation of cosmic sources of photons in the ~ 50 GeV to ~ 50 TeV energy range using Imaging Atmospheric Cherenkov Telescopes (IACTs). CTA will extend the range of these observations at both low and high energies, will improve their sensitivity by a factor of about 10 and will increase the precision of photon energy and direction measurements. This talk presents briefly the designs of the 23 m, 12 m and 4 m diameter IACTs that CTA will use to achieve this performance, before discussing the impact the array will have on studies of Fundamental and Astroparticle Physics. Topics covered include: searches for Dark Matter (DM) and axion-like particles (ALPs); studies of possible violation of Lorentz invariance; and studies of the sources and acceleration mechanisms of high energy cosmic rays.
Remember the Ellis/White paper.
Include EBL studies.

## Slide 2: Introduction – recent history
Eight months ago, we had a nearly complete telescope structure in Meudon (here on the occasion of the ESO visit)…
2

## Slide 3: Recent history
…and a multi-anode photomultiplier based camera, CHEC-M, in Leicester (here after installation of the Backplane, allowing self triggered operation).
3

## Slide 4: Building the GCT
These were put together in two and a half weeks of intensive work in November by a team of 17 people from the GCT camera and telescope groups.
Telescope structure:
  Cabling completed.
  Camera power supply installed.
  Camera cooling system added.
  Fibre for camera readout installed.
Camera:
  Function checked following transport.
  Installed on telescope.

## Slide 5: Installation of CHEC-M on telescope
Camera was mounted on telescope on 20th November.
Can now be done by 3 people in 15 mins (though it took a little longer the first time).
Arm lowered
Camera moved into position
Camera secured
Horizontal rods and cables attached
Camera raised
5
Richard White

## Slide 6: Camera function tests
  Camera tested on telescope (under shelter).
E.g. real time monitoring of TARGET module…
…and DACQ board temperatures.
LED flasher tests:
6

## Slide 7: First tests of the GCT prototype on sky
Thursday 26th Nov, night sky background 20 to 100 times higher than CTA site…

## Slide 8: First tests of the GCT prototype on sky
…but despite this successfully observed Cherenkov light from ~ 50 TeV showers, including this first event:
Note, high NSB required that MAPMs be operated ~ 200 V below voltage at which laboratory tests carried out – low gain, high threshold, no gain equalisation.
8

## Slide 9: First tests of the GCT prototype on sky
More events:
The cleanest event:
9

## Slide 10: CTA science meeting and inauguration of GCT

## Slide 11: Inauguration of the telescope
Party on 1st Dec. 2015.
Photo Akira Okumura
Helene Sol

## Slide 12: Outreach
First light and inauguration were the subject of CTA, Observatoire de Paris and STFC press releases.
And the inauguration was reported in at least one newspaper…
…who liked the colour we’ve chosen for the GCT:
« Un nouveau télescope flambant rouge a été inauguré ce mardi sur le site de l'observatoire de Paris à Meudon. »
12

## Slide 13: Progress with structure
At inauguration, telescope was moved by hand.
Damaged encoder caused control software to believe telescope was always “out of range”.
Hence drives locked by safety system.
Encoder now fixed.
Drive systems operating.
Can be controlled either remotely, or using switch box on telescope foundation.
Moving the GCT:
13
Jean-Laurent Dournaux

## Slide 14: Progress with structure
A programme of 330 tests has been devised to check the structure meets all specifications and requirements.
About 25% of tests started, some finished; goal is completion by end of summer.
Torque required for motion:
Telescope easily achieves required angular speeds.
Maximum power needed ~100 W per axis.
14

## Slide 15: Progress with structure
Check of optical/mechanical axis and mirror alignment.
Illuminate primary with green laser at 75 m distance.
Record image with CCD, with green filter to attenuate laser and reduce background due to stray light.
Red laser along mechanical axis.
Axes coincident and mirrors aligned within tolerances, without adjustment.
15
Squares of side 5 mm

## Slide 16: CHEC-M studies
Analysis of Paris data ongoing.
Here, graphical display of signal amplitude, with pulse traces in zoomed module view (MESS):
Times of pulse maxima.
BG signal maxima at varying times, peak signal for Cherenkov photons strongly correlated in time.
16
Richard White

## Slide 17: CHEC-M studies
CHEC-M now in MPI-K dark room.
Current tests focussed on data rate and integrity.
Less than 1 corrupt packet in 100M.
Occasional event building problems (0.1% of events) under investigation.
No packet loss with “CW” load at 85% of maximum link bandwidth.
Data through 1 DACQ board (15 TMs  120 packets per event)
Approximate limit for 15 TMs assuming 100% use of 2 x 1 Gbps on the DACQ (1050 Hz)
17

## Slide 18: CHEC-M next steps
Increase DAQ speed; read out all TARGET modules through one DAQ board with a 10 Gb/s link.
Allows CHEC to cope with goal data rates, with random spacing.
Shift to improved safety and control system (some safety critical boards not directly steerable, power to some boards not individually switchable).
Shift to new software release.
(Initiative to cooperate on camera software launched – Akira Okumura.)
Tests on telescope in September.
Planning CHEC-M tests on ASTRI.
18

## Slide 19: CHEC-S
SiPM window
Thermal break
Quickfit cooling connections
New heat exchanger
2 motors for dual door
Power relay
O-ring seals
Cooled focal plane
Improved door seal
19
Jon Lapington

## Slide 20: Mechanical design of CHEC-S
Larger enclosure (+3 cm/side), improved airflow.
Changes to body to simplify rack insertion.
O-rings for sealing, no flat gaskets.
Reposition DAQ boards.
Add further internal desiccator unit.
Improve heat exchanger.
Dual-panel door.
Further options under consideration:
  Revise telescope interface plate – thicker, more mounting holes.
  Add removable handles for lifting.
  Add a dry-nitrogen purging system.
Powder coat enclosure, passivate unpainted external areas.
20

## Slide 21: Mechanical design of CHEC-S
Major change in mechanical design: cooling of focal plane plate.
Thermal model showed SiPMs reach > 32 C in centre of camera.
Channel added around edge of plate.
“Gun drilling” provides path for cooling water through ribs.
Drilled channels for water cooling
Axial misalignment on 2 holes drilled for opposing directions = +/- 0.5mm (acceptable error/restriction)
21

## Slide 22: Mechanical design of CHEC-S
Studying window manufacture using hot slumping of ~ 2 mm thick glass.
Coat to improve UV transmittance and cut out NSB
Difficult, due to large range of angles of incidence on window (20° < q < 60°).
Alternatives, micro-lenses or Polycasa XT UV window.
Transmittance of coated window as function of wavelength and angle of incidence:
22
Paula Chadwick

## Slide 23: Front end electronics for CHEC-S
Recall T5 had low trigger threshold when no digitisation running, but poor dynamic range.
T7 improved dynamic range, but trigger problems worsened.
Noise in trigger caused by “substrate bounce”: digitisation influences analogue section of chip.
Split TARGET ASIC into two parts:
  Trigger (T5TEA) based on T5.
  Digitisation (TC) based on T7.
First studies show this combination satisfies our requirements.
Decide to use T5TEA and TC for CHEC-S, not T7.
T5TEA:
C.f. T5 with digitisation running:
Threshold 25 mV
Noise 5 mV
23
Stefan Funk

## Slide 24: Front end electronics for CHEC-S
Improve design of TARGET modules to further reduce noise.
Previous two boards become:
  Top Power Board.
  Central Auxiliary Board – shapers and trigger.
  Bottom Primary Board – digitisation.
Power Board under test.
Auxiliary Board schematics nearly ready.
Primary Board, layout ongoing.
Further mechanical and electronic improvement through using micro-coax cables to connect SiPMs + pre-amps to TARGET modules.
Ensure that module length allows CHEC-S to be compatible with ASTRI – drawings being re-checked.
24

## Slide 25: Back end electronics developments
Backplane firmware re-written:
Preparing for shift of Backplane construction to Amsterdam.
The prototype GCT camera timing board (shrunk version of the ZEN board from Seven Solutions)…
…will serve as a test-bed for the CTA universal timing card reference design.
plain code at lowest levels
Arnim Balzer
25

## Slide 26: Pre-production GCT
Downside of improvements to CHEC-S is that production is delayed – CHEC-S ready early 2017.
Upside is that expect only minor tweaks to CHEC-S to produce pre-production camera designs.
Some modifications to structure for pre-production:
  Accommodate common SST foundation.
  Cast some elements of structure.
  Cable housings will be plastic.
2015
Prototyping
Pre-Production
Production
2016
2017
2019
2018
2020
CHEC-M
On telescope (Nov 2015)
CHEC-S built
(Jan 17)
Prod Photosensor choice (March 2018)
2021
CHEC-S lab evaluation
(March 2017)
Pre-Prod Photosensor Choice (Oct 2016)
Overlap where procurement begins
Pre-Prod cameras on telescopes (July 2018)
1st Prod camera on-telescope and verified (March 2019)
Last Prod camera on-telescope and verified (Nov 2021)
Pre-Prod design complete
(June 2017)
2022
Richard White/Jean-Laurent Dournaux
26

## Slide 27: Summary
Tests of CHEC-M on the GCT prototype in Meudon have proven the GCT concept.
Good progress made with completion/testing of structure.
Noise problems in TARGET-based readout of camera solved.
CHEC-S design nearing completion: CHEC-S will be late, but will essentially be GCT pre-production camera.
Ambitious schedule sees 1st GCT on site in 2017, pre-prod (3 GCTs) completed mid-2018, prod (+ 32 = 35 GCTs) completed late 2021.
27
Cyril Trichard – can the GCT prototype see the Crab?