## Slide 1: PRINCIPLES OF NUCLEAR FISSION REACTORS
SUMMARY OF UNDERLYING PHYSICS
Neutrons can induce fission in heavy nuclei
~ 200 MeV is released per fission
~ 2.5 neutrons per fission are released
sF is large at certain energies
CHAIN REACTIONS
If no absorption or loss of
neutrons occurred then an
initial neutron in a block
of uranium can start a
chain reaction
For simplicity assume 2 neutrons per fission

## Slide 2: Fermi’s Chicago pile number 1 with alternating layers of uranium and graphite. On December 2nd 1942 Fermi slipped the control rods out of the pile generating heat.

## Slide 3
Define
REPRODUCTION CONSTANT ( MULTIPLICATION FACTOR) k
k > 1 ‘Super-critical’ – explosion (bomb)
k < 1 ‘Sub-critical’ – reaction dies out
k = 1 ‘Critical’ – stable chain reaction
Excess reactivity  dk = k - 1
k depends on many factors including the cross sections.
Natural Uranium (Infinite system) - No chain reaction possible
  As neutrons slow from 2 MeV to 1 keV sc becomes dominant over sf
Enriched Uranium (with 235U) Chain reaction possible
  For all values of Tn, sf (235U) > sc
  Shows basis for FAST REACTORS in which mostly high energy neutrons cause fission

## Slide 4
A simple matrix of natural (or slightly enriched U surrounded by a moderator
  FUEL: U (or less frequently Pu)
  MODERATOR: C, H2O or D2O to slow neutrons from ~2Mev to < 1 eV
  CLADDING: Contains fuel and prevents release of radioactive fission products + provides thermal contact with coolant
  COOLANT Gas or liquid, separated from fuel and moderator-.takes heat away from fuel for electricity generation
  CONTROL RODS Usually B (or Cd )with large sC for thermal neutrons to maintain k=1
  SHIELD Usually steel to contain pressure and concrete to give radiation protection
Conceptual diagram of
a basic thermal reactor

## Slide 5: Oldbury Magnox reactor 1968

## Slide 6
For n + U sR is negligible and the other cross sections (barns) as a function of energy are
Tn MeV | Isotope | sS | sf | si | sC
2 | 238U | 4 | 0.6 | 2.9 | 0.2
2 | NATU | 4 | 0.6 | 2.9 | 0.2
2 | 235U | 3.5 | 1.3 | 2.3 | 0
0.3 | 238U | 9 | 0 | 0.5 | 0.2
0.3 | NATU | 9 | 0.009 | 0.5 | 0.2
0.3 | 235U | 7 | 1.3 | 0.7 | 0
0.001 | 238U | 11 | 0 | 0 | 4
0.001 | NATU | 11 | 0.6 | 0 | 4
0.001 | 235U | 10 | 8 | 0 | 3
Thermal | 238U | 8 | 0 | 0 | 3
Thermal | NATU | 8 | 4.1 | 0 | 3.7
Thermal | 235U | 10 | 580 | 0 | 100
Remember that there are large resonances below 1keV

## Slide 7
ROLE OF THE MODERATOR
The moderator slows neutrons by elastic scattering
  E.g. General case :-
Let the masses of n and X be m and M respectively
In the Laboratory Frame X recoils in this process and so n loses energy in this frame
If we consider the process in the Centre of Mass System where n and X have equal and opposite momenta before and after scattering
   No loss of energy in this frame
Consider the transformation to the centre of Mass system travelling with speed VC

## Slide 8
In CMS mu1 + MuX1= 0 by definition
Also u1 = u - VC and uX1 = - VC
  Substituting for u1 and uX1 gives
  VC = u m / (m + M) and
  u1 = u M / (m +M)
Now consider the final velocities of
the neutron, v and v1 in lab. and CMS, and vX and vX1 the corresponding velocities for X.
In CMS mv1 + MvX1=0= mu1 + MuX1  |v1 | = |u1 | and |vX1 | = |uX1 |
The velocity v may be found from the following triangle of velocities using the cosine rule

## Slide 9
Substituting for VC and v1 we obtain
Let T0 and T1 represent the neutron K.E. before and after collision so T0 = ½ m u2 and T1 = ½ m v2
If A is the mass number of X then M=A u and m= 1 u
The maximum energy loss occurs when cos(q) = -1 with T1 a minimum
  i.e. q =1800 (head-on collision)
Experiment shows that the angular distribution of the neutrons is
isotropic in the C.M.S.

## Slide 10
Integrating over f gives :-
N.B. f is the azimuthal
angle and the –ve sign
occurs because T1
decreases as q increases

## Slide 11
For rapid moderation we need A as small as possible
  e.g. to reduce Tn from 2 MeV to 0.025 eV takes ~ 20 collisions for hydrogen but ~ 100 for carbon
Practical considerations for choice of moderator are
1) small A,
2) large sS, and
3) small sA ( = sC + sR)
CHOICES | H2O | D2O | GRAPHITE
sS (b) | 50 | 11 | 4.7
sA (b) | 0.66 | 0.001 | 0.0045
N.B. If H2O is used then U must be enriched with 235U because the absorption sA is large for H2O

## Slide 12: EXAMPLE: Compare the probabilities of traversing 1m of a) H2O, b) D20 and 3) Graphite without being absorbed. [Densities are:- a)1000 kg m-3, b)1100 kg m-3 and c) 1600 kg m-3]
P(x) = exp (-N s x)
H2O; NH2O = 1000 / ( 18 * 1.66 10-27) = 4.78 1028 m-3
PH2O = exp (- 4.78 1028 x 0.66 10-28) = 0.043
b) D2O; ND2O = 1100 / ( 20 * 1.66 10-27) = 3.31 1028 m-3
PD2O = exp (- 3.31 1028 x 0.001 10-28) = 0.997
c) Graphite; NC = 1600 / ( 12 * 1.66 10-27) = 8.03 1028 m-3
PC = exp (- 8.03 1028 x 0.0045 10-28) = 0.965