## Slide 1: SOLUTIONS OF THE REACTOR EQUATION
We shall need a value for the parameter LC for a reactor
First calculate LM for the moderator
Material | r kg m-3 | n (1028 m-3) | sf(b) thermal | sS(b) thermal | sA(b) thermal | SS (m-1) | SA (m-1)
graphite | 1600 | 8.23 | ----------- | 4.7 | 0.0045 | 37.7 | 0.037
235U | 18700 | 4.79 | 579 | 10 | 680 | 47.9 | 3229
238U | 18900 | 4.79 | ----------- | 8.3 | 2.72 | 39.8 | 13.0
  LM = [ 1 / (3 SA(M)SS(M) )]1/2 = 0.488 m so LM2 = 0.238 m2
  Assuming a value for the thermal utilisation factor f = 0.88
  LC2 = (1 – f) LM2 = 0.12 X 0.238 = 0.0286 m2

## Slide 2
So the volume is (3p2/B2)3/2 =73 m3
This is an underestimate and corrections need to be applied (later)
    i.e. B ~ 1.3 m-1
The Reactor Equation can be then be solved for a reactor with a given geometry
e.g. For a cube of side a, write the equation in cartesian coordinates
Note that the steady state equation implies a critical reactor and that the boundary conditions (F= 0 at edges) link the parameter B with the physical dimensions (just a in this case )

## Slide 3
This solution satisfies the boundary conditions given earlier
The minimum volume is given by
Solutions can be obtained for other geometries
SHAPE DIMENSIONS B2
1) Rectangular
Parallelepiped a, b, c
2) Cylinder R, L
3) Sphere R
Corresponding fluxes
and minimum volumes
The sphere offers the
minimum volume and least
surface area but is not very
practical
Cylindrical cores are more
usual

## Slide 4: EXAMPLE: A reactor core consists of a sphere of radius R. Show, by direct substitution or otherwise, that the solution of the reactor equation has the form where Assuming that the boundary condition is F = 0 at the surface of the sphere find R in terms of B. Calculate the value for the minimum volume V needed to provide a critical mass of fissile material assuming that [Assume that with spherical symmetry ]

## Slide 5
Boundary condition requires F= sin(Br) / r 0 at the
edge of the reactor when r = R so BR = p
= 3 x 0.05 x 0.4 x 35 so B = 1.45 m-1
So R = 2.17 m and the volume V = 4pR3 / 3 = 42.8 m3

## Slide 6
EXAMPLE:
For a cylindrical reactor core of length L and radius R
Express the volume of the core in terms of B and L.
By partial differentiation at constant B calculate the radius and volume
of the core which would give a critical mass of uranium in a graphite
reactor with

## Slide 7
Volume V = pR2L
So R = 1.7 m, L = 3.14 m and V = 28.5 m3

## Slide 8
MODIFICATIONS TO THE REACTOR EQUATION SOLUTION
MIGRATION LENGTH M
The distance travelled by the neutron to achieve thermalisation should be taken into account

## Slide 9
Example.
A spherical uranium – graphite reactor with a moderator to fuel ratio of 600 has a 235U enrichment of 1.6%.
[The values of k∞ and f are tabulated in table 10.4 (Lilley)]
Taking k∞ = 1.033, f = 0.834, LM2 = 0.265 m2 and
LS2 = 0.0368 m2 we obtain
B2 = 0.033/(0.166 X 0.265 + 0.0368) = 0.408 m2
The radius of the reactor = p / B = p / 0.639 = 4.9 m
The volume of the core is 493 m3
To find the mass of uranium first neglect its volume
Number density for graphite is 8.13 1028 m-3
Mass of uranium
= (8.13 1028 x 493 / 600 ) x 238 x 1.66 1027 = 26392 kg
= 26.4 tonnes

## Slide 10
BOUNDARY EXTRAPOLATION
Neutrons escaping the reactor boundary are not scattered so none return across the reactor surface
This effect is taken into account by extrapolating the boundary by d so
where Fa is the flux at the surface
A better efficiency can be achieved by surrounding the reactor with a Neutron Reflector which has sS>>sA (as for a moderator)
This effect is taken into account by extrapolating the boundary by d so that

## Slide 11
In the diagram d is enlarged for clarity
Adjust size of reactor until B2REFLECTOR = B2BARE
For BARE CORE
Flux F=cos(px/a’) where a’=a+2dBARE
For REFLECTOR
The new distribution has an exponential fall off in the reflector. Hence the core (with reflector) has a smaller ‘a’ for the same B2

## Slide 12
3) NON CRITICALITY
SUPERCRITICAL
SUBCRITICAL
Where Bg is GEOMETRIC BUCKLING
For a SUPERCRITICAL REACTOR B2M>B2g
For a SUBCRITICAL REACTOR B2M<B2g
and for a CRITICAL REACTOR B2M=B2g

## Slide 13: IMPROVEMENTS TO THE ONE GROUP MODEL
So far assumed that the neutrons have one velocity
  However Migration Length takes some account of the slowing down
For the One Group Model
There are more elaborate models which try to include neutron
moderation
TWO GROUP MODEL
Assumes neutrons have a single energy while slowing down and
then loses most of it to become a thermal neutron
FERMI AGE MODEL
Assumes that neutrons slow down continuously and not in
discrete steps

## Slide 14
The ‘AGE’ is the same quantity as L2SLOW
This is the simplest model which can account for resonance capture in 238U
This is a reasonable approximation for a reactor fuelled with
natural or slightly enriched uranium with a graphite moderator
  Not good for water moderators (light or heavy) since there are too few collisions
MONTE CARLO METHOD
A computer simulation following the life stories of individual
neutrons
  Random starting positions, energies, directions + collisions, absorption etc
Necessary for the accurate simulation of a real
HETEROGENEOUS reactor