## Slide 1: EFFECT OF DELAYED NEUTRONS
As we have seen the prompt lifetime of neutrons, 10-3 seconds, in a MAGNOX reactor leads to a very unstable situation as k changes
For FAST reactors T = 10-7 seconds and the situation is worse
Computers and electronics can respond in 10-6 seconds BUT CONTROL RODS CANNOT
The key to the control of reactors is the presence of DELAYED NEUTRONS
EFFECT OF DELAYED NEUTRONS
In 235U fission 0.65% of all neutrons arise from delayed emission.
The average mean life of the delayed neutron precursors is
= 12.5 seconds

## Slide 2
The mean lifetime is
(i.e. a weighted average)
This is much more easily controllable
  This is a critical number and is studied with much more detailed calculations
REACTIVITY CHANGES IN OPERATION
1. FUEL BURN UP (for thermal reactors)
For a hypothetical pure 235U reactor the fuel concentration and hence dk will reduce as the reactor burns fuel
  The fuel burn up is greatest at the centre where the neutron flux is highest
  Hence composition of the reactor varies non-uniformly and non-linearly with time
For normal thermal reactors using natural or slightly enriched U NEW fissile material 239Pu is constantly produced by breeding reactions

## Slide 3
The new 239Pu offsets the loss of 235U
  Extends useful life of fuel
  Produces more energy than is produced by 235U alone
Important reactions in fuel burn up are
n + 235U  FISSION or 236U
n + 238U  239U  239Np  239Pu
n + 239Pu  FISSION or 240Pu
n + 240Pu  241Pu
n + 241Pu  FISSION or 242Pu
241Pu fission is only important at the end of the fuel cycle at high burn up
The concentrations of 235U and 239Pu can be calculated i.e.

## Slide 4
Integrating these equations we obtain
where N0 is the initial concentration
The following graphs are examples for Fthermal ~ 1017 m-2 s-1
235
Some refuelling is required before ~ 2 years

## Slide 5: REACTOR POISONS
Many fission products (i.e. different neutron rich isotopes) are produced in reactors
Two products have huge capture cross sections for thermal neutrons and can effect reactor operations
  13554Xe81 sA=2.65 106 barns (cf sA= 190barns for 133 Xe)
  Yield = 0.064 atoms per fission
  14962Sm87 sA=5.8 104 barns (cf sA= 5.5barns for 154 Sm)
  Yield = 0.0113 atoms per fission
They are formed primarily from b decay
135Te 135I 135Xe 135Ce 135Ba
149Nd 149Pm 149Sm
The t1/2 values increase along the chains -- t1/2 = 9.2 hrs for 135Xe and 149Sm is stable

## Slide 6
135Xe is the main reactor poison and reaches a steady concentration after ~ 30 hours
  Causes dk to decrease by 0.03 for F~1018 m-2 s-1
  Need to build this amount of excess reactivity into the reactor
During normal operation (> 30 hrs) 135Xe is being produced as above. Equilibrium comes through losses via
  b decay
  The reaction 135Xe(n,g) 136Xe
However after shutdown the (n,g) reaction ceases so 135Xe starts to build up from 135I decay until the 135Xe b decay dominates
This poisoning implies that it is not possible to re-start a reactor until 40-60 hrs after shutdown
  Need to build in excess dk of 0.15 to cope with shutdown problems

## Slide 7
EFFECT OF 135Xe ON REACTIVITY
Consider a flux F ~ 1018 m-2 s-1
Excess reactivity of ~ 3% needed to overcome 135Xe during
steady operation
About 12% needed to enable the reactor to restart at any time
  In practice 15% is built in to allow for other poisons such
  as 149Sm
  149Sm has a build up time t½ ~ 53 hrs

## Slide 8
EFFECT OF 149Sm ON REACTIVITY
Consider a flux F ~ 1018 m-2 s-1
In an operating reactor the quantity of 149Sm grows until
production = destruction by neutron capture
If the reactor is shut down more 149Sm is created since
destruction stops i.e. no neutrons so no capture
An excess reactivity of dk~ 1.5% is needed to overcome this
when starting the reactor

## Slide 9: SHUTDOWN CHARACTERISITICS (Other than poisoning)
1. FISSION PRODUCT DECAY HEATING
There is a large energy release from the fuel after shutdown due to radioactive decay of accumulated fission products
Let F = fraction of power produced after shutdown
It is an important safety feature of power reactors that
coolant circulates after shutdown to remove heat

## Slide 10
2. DELAYED NEUTRONS
The reduction of neutron flux to near zero at shutdown will be significantly delayed by this source of neutrons
The neutron flux decays with a period equal to the mean life of the longest lived precursor (~ 80s)

## Slide 11: ACCELERATOR DRIVEN SYSTEMS
There are many advantages to be gained from accelerator driven systems
A 1 GeV proton beam ~ 10mA current generates neutrons (spallation) in a heavy target e.g.Pb or U. inside a fast breeder assembly
The coolant is metallic e.g. molten lead
The fast fission unit uses 232Th as fuel running at k ~ 0.95 !!
Each proton produces 13 fissions in the first generation, 13k in the 2nd, 13k2 in the 3rd etc giving a total of 13 / (1-k) fissions per proton.
At 200 MeV per fission and k=0.95 this gives an energy gain of 50!!
About 10-20% of this would be needed to power the accelerator

## Slide 12
Example of an accelerator
driven design
The schematic shown is a conceptual design
By C. Rubbia et al
CERN/AT/95-44 (ET)

## Slide 13
ADVANTAGES
Operates far from the critical condition
  No conditions in which self
  sustaining reactions are possible
  Reactor stops when accelerator stops
Breeds fuel and incinerates long lived wastes
  E.g. n + 232Th  233U chain
  May remove the need for geological storage of waste
REQUIREMENTS
Advance in cyclotron technology to deliver tens of milliamps at 1 GeV
  ~ 10 times current values but CERN are very confident it can be achieved
  An efficiency of 40 – 50% for converting electrical energy into beam energy

## Slide 14: Outlook for Fission Reactors
Economically nuclear power is compatible with fossil fuels in Europe but less so in the US due to differences in fuel costs
Environmentally nuclear power is good for low CO2 emission but the main concerns are:
  Risk of an accident – then the siting of the reactor, population distribution, prevailing winds etc. etc.
  Radioactive waste: high, intermediate and low level
  Stored on-site for several years in storage pools to remove heat and allow for the most intense activity to decay
  Then stored or reprocessed to recover U and Pu
  Remainder immobilised by vitrification into borosilicate glass, or incorporated in stable mineral lattices and stored in corrosion resistant cans in an underground depository

## Slide 15
Public opinion has a major effect on government decisions
  In a poll in europe in 2001 50% agreed to the nuclear power option if waste could be managed with 25% against
The desire for a secure energy supply and a reduction of CO2 emissions is causing nations to re-evaluate the nuclear power option
Country | (2005) Nuclear Generation | Number of Reactors |  | 
 | % Total Electricity | Operating | Being Built | Planned / Proposed
France | 79 | 59 | 0 | 2
Germany | 31 | 17 | 0 | 0
Japan | 29 | 55 | 1 | 12
Russia | 16 | 31 | 4 | 9
UK | 20 | 23 | 0 | 0
USA | 19 | 103 | 1 | 13
World | 16 | 441 | 27 | 153