## Slide 1: THE LAWSON CONDITION
Let fusion power PF= Pa + Pn
The neutron energy is given up to the lithium blanket and generates heat for the turbine while the as stop in the plasma and heat it.
Let PLoss be the net power lost through Bremsstrahlung, heat loss etc.
Let W = total plasma energy and Pi the external power supplied to heat the plasma
Then PLoss = W / tE where tE is the energy containment time
The Quality Factor Q = PF / Pi (26.1)
so ‘Break-even’ is when Q=1 and ‘ignition’ when Q = ∞
Under equilibrium conditions
dW/dt = Pa + Pi - PLoss =0
 Pinput  Pa + Pi = PLoss
and tE = W / PLoss
 Pa + Pi = W / tE (26.2)

## Slide 2
Define fa  Pa / PF = Ea / EF
(With notation change EF  QF in (25.3) to avoid confusion with Q)
and note that from eqn. (26.1) Pi = PF / Q
then eqn. (B) is equivalent to
(fa + 1/Q) PF = W / tE (26.3)
Now per unit volume from (25.3)
and W =2 x 3/2 n k T = 3 n k T so substituting we get
The Break-even condition Q=1 can then be written
(26.4)
THE LAWSON CRITERION
Since
The triple product ntET is often used to express this condition

## Slide 3
The requirement for ignition, Q = ∞, is
ntET ≥ 3 1021 m-3 s keV (T in keV)
For T = 10 keV and n ~ 1020 m-3 we see that the confinement time tE = 3 seconds for ignition.
EXAMPLE
A plasma contains a mixture of 50% D and 50% T at a temperature T = 20 keV. The average cross section for fusion is 2 barns.
a) Estimate the value of
If the energy produced per fusion is 17.6 MeV calculate the number density of the plasma that just satisfies the Lawson Condition given that the confinement time is 0.3 seconds.
b) What is the fusion power produced in this condition?

## Slide 4
Answer
a) At a temperature of 20 keV the velocity of the deuteron is given by
0.5 mD vD2 = 3/2 kT = 3/2 x 20 x 103 x 1.6 10-19 J
vD = [9.6 10-15 /(2 x 1.66 10-27)]1/2 = 1.70 106 ms-1
vT = [9.6 10-15 /(3 x 1.66 10-27)] 1/2 = 1.39 106 ms-1
Estimate relative velocity by assuming that on average the particles collide at 90o and ignore the centre of mass transformation. i.e.
so v = 2.20 106 ms-1
Hence = 2 10-28 x 2.20 106 = 4.4 10-22 m3 s-1

## Slide 5
Lawson Condition
(26.4)
Take fa = 0.2 and taking EF = 17.6 MeV (100% efficiency!) then
So n = 8.61 1019 m-3
Power so
PF = 2.30 106 Watts or 2.30 MW

## Slide 6: PARTICLE DENSITY
The value of n is determined by having a reasonable POWER DENSITY of
~ 40 MW m-3
  If the density is less than this linear dimensions become too large for economic operation ( e.g. need magnetic fields over too large a volume)
  If the density is larger than this,
    the pressure exerted by the plasma
  [ P=2nkT ~ 40 bar at T ~ 13 keV, n~1021 m-3] is too large [ e.g. needs B > 10T  see later]
    the neutron flux is too large for the reactor structure
With T = 13 keV, find that n = 3x1020 m-3 so that tC ~ 0.3 s to satisfy the Lawson Condition

## Slide 7: MAGNETIC CONFINEMENT OF PLASMAS
INTRODUCTION
No material container can withstand temperatures ~ 108 K!
Plasmas contain both positive and negative ions
They cannot be confined by electric fields since forces on ion types will be equal and opposite
Most promising approach is to confine plasmas using magnetic fields
We will
  Review the motion of charged particles in a magnetic field
  Consider the optimum field configuration
  Translate the description of the motion of individual particles into the macroscopic concept of pressure

## Slide 8: CHARGED PARTICLES IN A MAGNETIC FIELD
Basic equation for the interaction of a charged particle with a magnetic field is :- (26.5)
Consider a uniform magnetic field along the z axis
 B = (0 , 0 , Bz)
The solution  vx = v0 sinwt, vy = v0 coswt and vz = constant.
Integrating x = +(v0/w)coswt, y = -(v0/w)sinwt and z = constant x t
This motion is in a HELIX. In the x-y plane motion is in a circle
of radius a with angular velocity w

## Slide 9
x2 + y2 = a2 = v02 / w2 where
v02 = vx2 + vy2
+ve and –ve ions e.g. 20 keV D+, B=10T  a = 2.3mm
MAGENTIC FIELDS, PARTICLE DENSITY AND PRESSURE
Above considerations indicate that it is possible to confine a single charged particle
For a plasma at high T the K.E. of the ions exerts a pressure tending to blow the plasma apart
  The magnetic field must balance this pressure

## Slide 10
Pressure = force / unit area
  P = F / unit volume
   Pi = ni e vi  B ions
  Pe = - ne e ve  B electrons
  (where ni and ne are the relevant particle densities)
Write n = ni + ne ; P = Pi + Pe
P = n e (vi – ve)  B
 P = j  B
Where P is the MAGNETIC PRESSURE and j is the CURRENT DENSITY
Using Maxwell’s Equations
    B = m0 j
  P = 1/m0 (  B )  B
  = 1/m0 [ - ½ B2 + ( B .) B]
[Using the vector identity
(u.v)=v.u + u.v +v  u + u v ]

## Slide 11
If the radius of curvature of B >> length over which B changes then
If the plasma is entirely contained by the magnetic field then P0 outside.
Use labels ‘in’ and ‘out’ to label inside and outside of the plasma then Pin = B2out/2m0 – B2in/2m0
If no magnetic field penetrates the plasma (i.e. perfectly diamagnetic) then Bin = 0 and the maximum pressure sustained is Pin(max.) = B2out/2m0 =2 n k T (2 factor for ions + electrons)
For Bout = 2 tesla  Pin ~ 15 bar;
kT = 10 keV  n = 5 x 1020 m-3 which gives a reasonable power density
(26.6)

## Slide 12
N.B. If Bin  0 then B2out > 4m0 n k T
The ratio b = Pin / (B2out/2m0 )
= 4m0 n k T / B2out
is called the BETA FACTOR for the plasma.
Using Pin = B2out/2m0 – B2in/2m0
we can write b = 1 – (Bin / Bout)2:
and Pin = b (B2out/2m0) (26.7)
i.e b is a measure of the penetration of the magnetic field into the plasma.
If b  0.1 the plasma is called ‘low b ‘ otherwise ‘ high b ‘