## Slide 1: REACTOR ACCIDENTS
1. CHERNOBYL
RMBK design has several weaknesses including
  No secondary shutdown system
  Ability to over ride safety trips easily!
  Less stable than western reactors
  Graphite runs at > 700oC (burns in air!)
  Reactivity worth of control rods inadequate

## Slide 2
Attempted a test to check whether the emergency cooling system was OK!!
  To be carried out in a shutdown
  Delayed to night shift due to order to provide power on day shift
Started with staged power reduction from 3200MW
  Reduced in error below 30 MW
  Badly poisoned with 135Xe
  Should have abandoned test here
Control rods withdrawn to raise power to 200MW
Standby coolant pumps started
  Power at 7% and cooling at 120%!!
  Very sensitive k~10-1 and T~1s
Problem with steam drum level (low)
  Reactor trip signal disabled!!
  Manual top up with cold water
  Fall in core temperature control rods out to furthest limit
  Reactor uncontrollable
Crew decide to start the test!!!

## Slide 3
Cut off steam supply to the turbine ( no heat sink) after disabling the safety reactor trip
  Steam fraction increases
  k and f increase too rapidly for automatic control rods
  Panic button pressed when P > 320MW but control rods are too few and too slow
1St surge of power boils
  Cooling water cannot take away heat
  Fuel disintegrates and coolant boils
Final surge of power > 3000MW
  Steam explosion
  Hydrogen (from zirconium-water and water-graphite reactions) explodes
  Graphite ignites
World’s worst nuclear accident

## Slide 5
2. THREE MILE ISLAND (1979)
The accident involved the loss of coolant to a PWR due to a failure in the feed--water system
  Reactor and turbine tripped off
  Problem handling residual heat led to temperature rise in the core and a 20% core meltdown
  Volatile fission fragments contaminated the primary coolant which, due to pressure, vented a quantity of material into the atmosphere
Many lessons were learned about reactor design, human misjudgement and the malfunction of pumps and valves.
3. WINDSCALE (1952)
An air cooled reactor built solely to manufacture plutonium
Some release of radiation into the atmosphere due to limited instrumentation and the not well understood Wigner effect (radiation damage to graphite)
Not really relevant as a safety issue today

## Slide 6: HEALTH HAZARDS ASSOCIATED WITH RADIONUCLIDES
All radiation is dangerous but some radionuclides are especially so as their chemistry allows them to get into the food chain
Strontium–90 (and 89Sr)
  is absorbed in plants from soil or by foliar deposition, and then passed to diary products. Absorbed into bone because chemically is calcium-like.
Cesium-137
  tightly bound by soil but contaminates food by foliar absorption. Chemically potassium-like.
Carbon-14
  readily passes into biological systems
Radioiodine (131I) (F-, Cl-like)
  ingested through drinking milk and concentrates in thyroid gland.

## Slide 7: Natural Radioactivity
Some radionuclides occur naturally as single isotopes (of cosmic and terrestrial origin). Others are components of three distinct chains of radioactive elements:
(1) The uranium series which originates with 238U
(T1/2 =4.5 x 109 years)
(2) The thorium series which originates with 232Th (T1/2 =1.4 x 1010 years)
(3) The actinium series which originates with 235U (T1/2= 7.0 x 108 years)
These 3 families of radioactive heavy nuclei are found in the earth’s crust and account for much of the radioactivity to which man is exposed.
A fourth family, the neptunium series – parent 241Pu (T1/2 = 14 years) once existed but the parent and subsequent daughters have short half lives; only 209Bi (T1/2 = 2 x 1017 years) remains.

## Slide 8: SECULAR EQUILIBRIUM
Uranium series has
238U  234Th *  234Pa * etc.
(T1/2 =4.5 x 109 years) (T1/2=6.7 hours) (T1/2=24 days)
(1) (2) (3)
Rate of decay of (1)  dN1/dt = - 1 N1 ----- (A)
Rate of decay of (2)  dN2/dt = 1 N1 - 2 N2 ----(B)
(1st term is rate of formation from (1); 2nd term is decay of (2))
Rate of decay of (3)  dN3/dt = 2 N2 - 3 N3 -----(C) etc.
N1 N2 N3 are the number of radioactive atoms (1) (2) (3) at time t
Solve (A)  N1 = N10 exp(-1t)
where N10 = number of (1) atoms at t=0

## Slide 9
Solve (B)  dN2/dt = 1 N10 exp(-1t) - 2 N2
Multiply both sides by exp(2t) and note that
d (N2 exp(2t) )/dt = dN2/dt . exp(2t) + 2N2 exp(2t)
Substituting for 2N2 exp(2t) we have
d (N2 exp(2t)) /dt = 1N10 exp{(2 - 1) t}
or d (N2 exp(2t) )= 1N10 exp{(2 - 1) t]}dt
Integrating between 0 and t, we have
{[ N2 exp(2t) ]t - [ N2 exp(2t) ]0 =
{[1N10 exp{(2 - 1) t}]t – [1N10 exp{(2 - 1) t} ]0}/ (2 - 1)
So N2 exp(2t) – N20 = 1 N10 . (exp{(2 - 1) t} – 1) ) /(2 - 1)
Multiply through by exp(-2t), and noting that N20 = 0 :
N2 = 1 N10 . (exp(-1t) - exp(-2t)) /(2 - 1) +

## Slide 10
Assumption that is true for actinide series T1/2 (1) >> T1/2 (2)
 1 << 2 since 1 = ln2 / T1/2 (1) and 2 = ln2 / T1/2 (2)
 at large enough t we can neglect exp(-2t) compared with exp(-1t)
 N2  (1/2) N10 exp(-1t) = (1/2) N1
 1 N1 = 2 N2
and using (B) dN2/dt = 1 N1 - 2 N2 = 0
Using (C) dN3/dt = 2 N2 - 3 N3 = 1 N1 - 3 N3
Using same arguments as before
1 N1 = 3 N3 and dN3/dt = 0
 1 N1 = 2 N2 = 3 N3 = … etc. called secular equilibrium
i.e. dN/dt = 0 for all members of series except first
Note that activity of any of the daughters is given by i Ni = 1 N1
i.e. is the same for each nuclide in the chain.

## Slide 11: Example
Uranium series has
238U (T1/2 =4.5 x 109 years) decaying to
234Th * (T1/2=6.7 hours) decaying to 234Pa* (T1/2=24 days)
A sample of rock contains 1kg of 238U. What numbers of 234Th * and 234Pa atoms would you expect to find?
Assume secular equilibrium and l = ln(2)/T1/2
So NU/(4.5x109 x 365 x 24) =
NTh/(6.7) =
NPa/(24 x 24)
NU = 1 / (238 x 1.66 x 10-27) = 2.5 x 1024
So NTh = 4.2 x 1011
and NPa = 3.7 x 1013