## Slide 1: URANIUM SERIES
Found in many rocks and soils.
  Granite contains about 4 ppm.
  Phosphate rock found in Florida contains 120 ppm  can be found in food chain due to phosphate fertilisers.
Series contains , ,  emitters.
  Series decays through radium-226 (T1/2 = 1600 years) which  decays to radon-222 (T1/2 = 3.8 days) – a noble gas.
Activity of any daughter nuclei in series is:
  i Ni = 1 N1 where  = ln2/T1/2 and ‘1’ is 238U in this case.
Average level of radon gas in UK houses is 20 Bq/m3
  The effective dose equivalent = 1.3 mSv/year
  Varies with location – It can be up to 6.4 mSv/year in Cornwall
  (must consider lung dosimetry, occupancy and other factors)

## Slide 2
National Radiation Protection Board recommends that action should be taken if level is 200 Bq/m3 (equivalent to 10 mSv/year)
  and that the design level limit is 100 Bq/m3 for new houses.
Parts of the country with > 1% probability of homes being above the action level should be regarded as affected areas.
  Effective dose in a lifetime should be less than 75mSv, i.e. at 10mSv/year homeowner should take action within 7 years.
Total energy deposited by daughters ~ 500 times that from radon
  radon and daughters are electrically charged when formed,
  attach to dust particles than can be inhaled, and a fraction will remain in lungs that decays to solids and stays there (radiation weighting factor for  particles = 20).
226Ra is the parent of radon and is similar to calcium in its chemistry
  collects in bone.
  Granite contains ~ 40 Bq/kg of 226Ra.
  Brazil nuts contain ~ 500 Bq/kg, extraordinarily high.

## Slide 4
Thorium Series
Thorium is relatively insoluble, low specific activity, not usually detected in biological samples.
Series decays through 228Ra which  decays to 228Ac and 228Th then  decays to 224Ra and 220Rn whose half-life is 56 seconds.
Because of its relatively short half-life, the atmospheric concentrations of 220Rn are very much less than 222Rn produced by the uranium series
   the dose from this isotope and its daughters is much less.
Actinium Series
235U is only 0.7% of natural uranium, and the series decays through 219Rn whose half life is 4 seconds. Negligible contribution to environmental radiation.

## Slide 7
Other Natural Radioactivity
40K isotope of potassium – 40K, has T1/2 = 1.3 x 109 years. ~ 0.01% of natural potassium.
Emits ’s, 1.3 MeV max, and 1.461 MeV -ray.
The potassium content of soils is controlled by fertilisers.
70 kg man contains ~ 140g of potassium mainly in muscle (activity of 3.7 kBq) giving equivalent dose rate of ~ 0.2 mSv /year to reproductive organs and soft tissue and ~ 0.15 mSv/year to bone.
40K is the predominant radioactive component in normal foods and human tissue.

## Slide 8
Cosmic Rays
Primary radiation, above atmosphere, contains highly energetic (up to 1020-21eV) particles ~ 85% protons, 14% -particles and 1% heavier particles having Z= 4 – 26
Interactions with atmosphere produce electrons, -rays, neutrons, muons.
  At sea level, ~ 80% muons, 20% electrons.
A number of radionuclides that exist on earth are due to the interaction of cosmic rays with atmospheric nuclei
  most important are tritium (3H), 14C and 7Be.
Tritium is a very low energy -emitter. Whole body dose ~ 0.03 – 0.06 Sv/year.
14C – another low energy -emitter.
  Total carbon content of 70 kg man ~ 18%.
  Dose is 14 Sv/year to the body tissues , ~ 7Sv/year to reproductive organs.
  This can rise to 10 Sv/hour at polar latitudes (increased cosmic ray activity) and at high altitudes (e.g. Concorde flights).
  Solar flares can give much higher doses.
Total dose is typically about 2.6 mSv/year with 85% from natural radioactivity & 15% from artificial sources (mainly medical)

## Slide 9
Source | Effective dose mSv / yr | Range mSv / yr
Natural sources (85%) |  | 
Cosmic rays | 260 | 200-300
Food and drink | 300 | 100-1000
Radon | 1300 | 300-100000
Terrestrial g rays | 350 | 100-1000
Subtotal | 2210 | 
Artificial sources (15%) |  | 
Medical | 370 | 
Other | 6 | 
Subtotal | 376 | 
Occupational (0.3%) | 8 | Up to 20 mSv for a few
TOTAL | 2600 | 
Special groups |  | 
Radon prone areas | 5000 | 
Nuclear industry | 1000 | 
General radiation workers | 500 | 
Medical radiation workers | 100 | 

## Slide 10: Radiation Protection: Practical Advice
Aims:
(a) Radiation protection is based on the
ALARA principle – dose rates should be
As Low As Reasonably Achievable.
(b) Ensure use of radiation is justified –
produces net positive benefit.
Use time, distance, shielding to achieve dose reductions.
1. Reduce time in contact with radioactive material:
  Rehearse procedures with non-radioactive material
  Use smallest amount of radioactivity possible
    Can experiment be done with less hazardous material?
  If contaminated, wash with soap and water. Remove contaminated clothing to bag and monitor activity

## Slide 11
2. Increase Distance
Radiation/unit area at R from source I0
= I0 / 4R2
 Radiation intercepted at R from source I0
= I0A / 4R2
Increase distance from 1cm to 10 cm decreases exposure by 100 - use forceps or long tongs to reduce dose to fingers.
Geiger counters, NaI detectors or dose meters give present measure of dose rate – film badges only tell history.

## Slide 12
3. Shielding
  safety glasses, disposable gloves, use forceps -  sources sometimes creep due to radon and recoiling nuclei.
  1 cm of perspex stops s and contamination – use disposable gloves.
  lead blocks ~ 10cm thick will reduce exposure from most sources by at least a factor of 10. Strong sources are usually at the end of a long holder.
Internal contamination
(inhalation, ingestion)
Avoid or limit by containment – use fume cupboard in laboratory situation.

## Slide 13
PROBLEM
  What thickness of concrete is needed to attenuate a collimated beam of 1 MeV photons by a factor of 106?
    Density rconcrete = 2200 kg m-3
    Mass attenuation coefficient is mm = 0.064 cm2 g-1
SOLUTION
m = r mm = 2200 x 103 x 10-6 x .064 cm-1
=0.141 cm-1
exp(- m x) = 10-6
so x = 98 cm