## Slide 1: NEUTRON CYCLE IN AN INFINITE THERMAL REACTOR
A THERMAL REACTOR contains 235U and 238U
Thermal neutrons induce fission in 235U
  ½ mv2 ~ kT ~ 0.025 eV at 20oC  v ~ 2200 m s-1
Consider M neutrons of energy ~ 2 MeV produced by the thermal fission of 235U and consider the possible reactions they can undergo. Define :-
FAST FISSION FACTOR e
Possibility that a few fast neutrons cause (Fast) fission in 238U
e is fraction slowing down below 1 MeV
(below which sf  0 for 238U)
RESONANCE ESCAPE PROBABILITY p
Some neutrons are captured in 238U resonances
p is the fraction that escape capture while slowing down and increases as the moderator to fuel ratio increases

## Slide 2
THERMAL UTILISATION FACTOR f
f is the fraction of thermal neutrons absorbed in the fuel (i.e. they escape capture in moderator or coolant)
Note that f decreases as the moderator to fuel ratio increases
FUEL UTILISATION FACTOR h
h is the average number of fission neutrons produced per
neutron absorbed in the fuel

## Slide 3: EXAMPLE:- Calculate h for natural uranium for induced fusion with 2 MeV neutrons and thermal neutrons. Assume that 2.5 neutrons are produced for each fission and that the fission and capture cross sections in barns are :- 238U 235U sf sC sf sC 2 MeV 0.6 0.2 1.3 0.0 Thermal 0 3.0 580 100
h= n x sf / sA = n x sf / (sf + sC) for the fuel
For UNAT (2 MeV) sf = 0.007 x 1.3 + 0.993 x 0.6 = 0.60
and sC = 0.007 x 0.0 + 0.993 x 0.2 = 0.199
So h= 2.5 x 0.60 / (0.60 + 0.199) = 1.88
For UNAT (Thermal) sf = 0.007 x 580 + 0.993 x 0.0 = 4.06
and sC = 0.007 x 100.0 + 0.993 x 3.0 = 3.68
So h= 2.5 x 4.06 / (4.06 + 3.68) = 1.31

## Slide 4
So for an infinite system (no losses from leakage) the reproduction constant is
SCHEMATIC OF ONE CYCLE
For finite systems extra factors must be included to allow
for leakage of neutrons

## Slide 5: Optimising the Design
The parameters f, p, h and so k∞ depend on the moderator to fuel ratio NM / NF, enrichment of the fuel and also the geometric design of the reactor.
For homogeneous reactors a chain reaction is not possible for a natural uranium-graphite reactor. (It is using UO2SO4 with D20).
  e.g. For NM / NF = 300:-
  f=0.85, p= 0.66, h= 1.33 yielding k∞ = 0.744
Increasing the ratio NM / NF increases p and reduces f
Concentrating the fuel into rods reduces the absorption and so increases p .
An optimised design using fuel rods in a graphite moderator yields a chain reaction in a natural uranium-graphite reactor.
  e.g. Calder Hall and Fermi’s first reactor in Chicago

## Slide 6
TYPICAL VALUES
e ~ 1.02
i.e..2% extra neutrons from fast fission in 238U
p ~ 0.88
i.e..12% neutrons are captured in resonances 238U
238U(n,g)239U then (b-) 239Np and (b-) 239Pu
f ~ 0.88 For MAGNOX reactors
~ 0.66 For AGR (sC in stainless steel)
h ~ 1.33 For MAGNOX reactors
~ 1.77 For AGR (2.3% 235U)
Enriching the fuel from 0.7% to 1.6% changes h from 1.33 to 1.60
  For a homogeneous U - graphite reactor this increases k∞ from 0.75 to 1.03
  The MAGNOX reactors use UNAT with a lattice structure

## Slide 7
LEAKAGE IN FINITE SIZE REACTORS
FAST NON-LEAKAGE PROBABILITY PNLf = fraction of neutrons which do NOT leak out of the reactor as they are slowing down
2) THERMAL NON-LEAKAGE PROBABILITY PNLTh is the fraction of THERMAL NEUTRONS which do NOT leak out of the reactor
Thus the EFFECTIVE REPRODUCTION CONSTANT for an OPERATING REACTOR is
ENERGY PRODUCTION
The maximum reasonable power density is ~ 50 MW / m3
limited so that
  heat can be removed safely
  neutron flux does not destroy the structure
Let f be the flux density of neutrons (m-2 s-1)
Then Fission Rate = f A N sf dx where
  A is area over which flux exists
  N is No. of fissionable nuclei ( 0.7% in UNAT) and A dx = dV

## Slide 8
So Fission Rate per unit volume = f N sf
For natural uranium A~238 and density rU = 20000 kg m-3
so N = 0.007 x 20000 / (238x1.67 .10-27)
= 3.5 1026 m-3
sf = 577 barns for thermal neutrons + 235U
Take energy per fission Ef ~ 200 MeV
Then Rate of Fissions R = 50 MW m-3 / Ef = f N sf
R = f x 3.5.1026 x 577.10-28 = 50.106 / (200 x 1.6.10-13)
Then f ~ 1017 m-2 s-1
CONSUMPTION OF 235U
For 50 MW m-3 need 50 106 / (200 106 x 1.6 10-19)
= 1.56 1018 fissions s-1 m-3

## Slide 9
Expressed in mass of 235U per day :-
1.56 1018 x 235 x 1.66 10-27 x 3600 x 24
= 0.053 kg m-3 / day consumed by fission
Some 235U is consumed by neutron capture as sC = 101 barns
  Allow for this by scaling by (sf + sC) / sf
  Total consumption of 235U is 0.053 x (sf + sC) / sf
  = (577+101) / 577 x 0.053
  = 0.062 kg m-3 / day
  COMPARISON WITH OTHER FUELS
The raw cost of natural uranium is ~ 90$ per kg
  However enrichment and fabrication of fuel rods leads to a cost of ~ 0.4p / kW hr
  This compares to ~1.5p / kW hr for coal
    These figures assume an efficiency of ~34% and are a snapshot in time. They will vary with time.

## Slide 10
The main overall cost / kW hr is dominated by the capital cost of the nuclear plant (decommissioning costs included) over 25 years
  Typically capital expenditure is ~ 60% of the cost and fuel ~ 18%
Other technologies incur additional charges
  Coal and gas will incur costs for reducing the CO2 in the range of £0 - £30 per tonne
    ~28% capital / 34% fuel / 23% CO2
  Wind power must include back-up capacity
    ~ 52% capital / 30% standby
The above fractions were taken from a report from the Royal Academy of Engineering 2004 ‘The Cost of Generating Electricity’

## Slide 11
This and other reports are reviewed in ‘The Economics of Nuclear Power’, Uranium Information Centre Ltd
http:// www.uic.com.au/nip08.htm
The following table is from the Royal Academy of Engineers 2004
  Costs will vary over time and country (e.g. see p 235 in textbook)
Present day costs of generating electricity
(p / kW hr) from new plant
 | Basic cost | With Back-up | With CO2
Nuclear | 2.3 | N/A | N/A
Gas | 2.2 | N/A | 3.4
Coal | 2.5 | N/A | 5.0
Wind on-shore | 3.7 | 5.4 | N/A
Wind off-shore | 5.5 | 7.2 | N/A

## Slide 12: EXAMPLE:- Define the ‘Thermal Utilisation Factor’ f. A reactor consists of a homogeneous mixture of natural uranium and graphite with a ratio of 200 : 1 carbon atoms to uranium atoms. Calculate a value for f assuming that all other components in the reactor may be neglected. [ Natural uranium is 99.3% 238U and 0.7% 235U . Assume sA(235U)= 678 b, sA(238U)= 2.75 b and sA(12C) = 0.0045 b.]
The thermal utilisation factor f is the fraction of thermal neutrons
absorbed in the fuel
(i.e. escaping capture in the moderator, cladding or coolant)

## Slide 13: EXAMPLE:- A natural uranium thermal fission reactor operates at a thermal power output level of 2 GW. Calculate the rate of 235U undergoing fission per second assuming that the energy release per fission is 200 MeV. Calculate the rate of production of 239Pu in kg/yr due to thermal neutron capture only assuming that all the neutrons captured in 238U lead to the production of 239Pu. [ Assume that for thermal neutrons 235U has a fission cross section sf = 580 b while 238U has a capture cross section sc = 2.7 b. Natural uranium contains 0.7% of 235U ] .

## Slide 14
Consumption of 235U by fission NF = 2(GW) / 200 (MeV / fission)
= 2 x 109 / (200 x 1.6 x 10-13) = 6.25 x 1019 atoms / second
For the fission reaction NF = F x sF(238U) x N235
where N235 is the number of 235U atoms
For production of 239Pu Nprod= F x sC(238U) x N238
where N235 / (N235+ N238) = 0.007 so N238 / N235 = 141.9
Nprod / NF = F x sC(238U)x N238 / F x sF x N235 = 141.9 x 2.7 /580 = 0.66
No. atoms of 239Pu per second = 0.66 x 6.25 x 1019
= 4.12 x 1019 atoms per second
So mass of 239Pu produced per year
= 4.12 x 1019 x 1.66 x 10-27 x 239 x 60 x 60 x 24 x 365.25 = 516 kg yr-1