## Slide 1: Characterization of Silicon Photomultipliers for beam loss monitors
Lee
Liverpool University weekly meeting

## Slide 2: What I will talk about
Short introduction about me
What are SiPMs and their uses
Experiments performed
Results and implications

## Slide 3: Beam Loss monitoring
Due to the size of proposed linear colliders, what is required is a beam loss monitor that can span long lengths for beam alignment and machine protection.
One proposed method is optical fibers along the beam line
Charged particles may cross these fibers inducing Cherenkov radiation which may be trapped within the critical angle of the fiber and travel down the fiber.
A detector is placed at the end of the fiber.
A detector with large dynamic range is required .
One option is to use a Silicon Photomultiplier (SiPM)

## Slide 4: Principles of SiPM operation
π
P+
n+
P
hole

## Slide 5: Principles of SiPM operation
Output is quenched passively by a resistor
Quenching reduces output to original state and the process can start again
An SiPM is covered in these cells.
The general shape of the SiPM output is given by the rise time of a signal and the quenching time of the output falling back to zero

## Slide 6: SiPMs
Compact
  From 1 to 3.5 mm2
Insensitive to magnetic fields
Low operational voltage
  Tens of volts
Versatile
  Widely used
Cheap
  $100’s per detector
A collection of mounted SiPMs
Array of cells and quenching resistors

## Slide 7
SiPMs under consideration
Two prototype SiPMs were considered
1.STMircoelectronics – Module H
2.Hamatsu – S10362- 11-100C
Both SiPMs have different architecture and very different bias voltages

## Slide 8: Experiments undertaken
Total noise
- To define count rate plateaus
After pulsing
- Not essential for characterisation but interesting to observe after pulsing
phenomenon
Time and Spatial resolution
- To benchmark detector limits for triggering a signal
Photon resolving power
  - To find the maximum/minimum detectable photons

## Slide 9: Equipment and layout
Fan to cool modules
NIM modules
SiPM
Counter / power generator
LED

## Slide 10: Experiment 1 – Total noise
First experiment was designed to measure the dark count from the SiPM.
Dark counts come from various sources but high proportion are from thermally induced electrons which cause an avalanche
This was done by activating the SiPM without firing

## Slide 11: Total noise results (ST module H)
9/18
ST module H

## Slide 12: Total noise results (Hamamatsu)
Overall results

## Slide 13: Experiment 2 – After pulsing
After pulsing is an effect caused by impurities in the SiPM
Electrons become trapped in the device
Released about 100ns later causing an avalanche and a signal after the main signal
To characterise the SiPM for after pulses, the number of pulses within a 100 micro seconds window and moving the start of this window along
We want to count the number of pulses in this region
Window width 100 micro s
Main pulse
Time delay between window and main pulse
10/18

## Slide 14: Experiment 2 – After pulsing
SiPM
Amplifier
Counter
Inverting i/o
Linear fan out
Discriminator
Gate generator / delay module
AND gate
Discriminator
11/18

## Slide 15: Experiment 2 – After pulsing results
Chart: Number of counts for increasing delay of 100 microsecond gate
| 34 | 47 | 60 | 70 | 80 | 90 | 100 | 125 | 150 | 175 | 200 | 225 | 250 | 275 | 300 | 325 | 350 | 375 | 400 | 425 | 450 | 475 | 575 | 675 | 1000
 | 75708 | 71925 | 68244 | 57076 | 55711 | 55546 | 44400 | 35960 | 31395 | 28647 | 27461 | 25641 | 24078 | 23683 | 22769 | 21978 | 22174 | 21409 | 21140 | 21135 | 21064 | 22541 | 22558 | 22663 | 22836
12/18

## Slide 16: Experiment 3 – Time resolution
An important quantity is the resolution of the SiPM as this links to spatial resolution to BLM
What affects the resolution of the SiPM
Charge collection time ~ 10ps
Avalanche propagation time ~ 10’s ps
Electron drift time ~1ps
Read out electronics ~10’s ns(major)
The sigma of the distributions indicates the temporal uncertainty

## Slide 17: Experiment 3 – Time resolution
oscilloscope
SiPM
Linear fan out
Discriminator
Gate generator
TDC
Amplifier
LED
Pulse generator
Start signal
Stop signal

## Slide 18: Experiment 3 – Time resolution

## Slide 19: Experiment 4 – Spectrum
The final and longest experiment was the spectrum measurement
The SiPM was left to fire pulses for a long period of time
The signal is converted to digital such that the entire spectrum of SiPM output pulses is recorded.
Charge spectra greatly influenced by :
1) Bias voltage
2) Light source intensity
The output of a charge spectrum should (in theory) result in multiple peaks representing multiple cell activation. However due to noise etc the distribution is more a convolution of a Poisson distribution from cells firing and a Gaussian distribution due to noise etc

## Slide 20: Experiment 4 – Spectrum
SiPM
Gate generator
ADC
Amplifier
LED
Pulse generator
Delay module 45 ns

## Slide 21: Experiment 4 – Spectrum
ST
Hamatsu

## Slide 22: Experiment 4 – Spectrum
The resolving power is the number of measured photons , where the separation between two consecutive peaks is three times the variance.
The peak resolution is two times the variance
Resolution power of both SiPMs with and without fiber

## Slide 23: Thanks for listening
Special thanks to Marco Panniello