## Slide 1: Lecture 9
In this lecture we will look at:
  Charges and currents.
  Current density.
  The drift speed of charge carriers.
  Resistance and resistivity.
  Ohm’s Law.
  Conduction in metals.
  Power in electric circuits.
  Semiconductors and superconductors.
After this lecture, you should be able to answer the following questions:
The drift speed of the electrons carrying an electric current in a copper wire is typically only about 10-3 ms-1. Why then does a light come on almost instantaneously when the switch is depressed even though it is 5 m away from the bulb?
What is the difference between resistance and resistivity?
Give three formulae for the power dissipated in a resistor R across which there is a potential V and through which a current i is flowing.

## Slide 2: Charges and Currents
Move from consideration of electrostatics to study of electric currents and their effects.
Consider first steady (“direct”) currents.
For current to flow must be a net flow of charge.
Electrons in an isolated loop of copper wire travel at about 106 ms-1, but no net flow of electrons, so no current.
Add battery to produce current:
Charges move because electric field, E, established in copper and charges (electrons) feel force, F = Eq.
Current through plane
If i constant, i = q / t [9.2]
Charge from current through:
If i constant, q = i t [9.4]
+ -
i
A

## Slide 3: Current Density and Drift Speed of Charge Carriers
Unit of current is ampere (A = C s-1).
Current direction taken to be direction in which +ive charge travels.
Arrows often used to indicate current direction, but current is scalar, not vector quantity.
Current density is vector quantity with direction given by that of the velocity of the moving +ive charges (or opposite to direction of velocity of –ive charges).
Magnitude of is current per unit area.
Units of current density, A m-2.
Hence calculate current from current density:
If current is uniform and perpendicular to area A, J = i/A [9.6]
In metals, current is due to drift of electrons.
If there are n charge carriers per unit volume, sum of charge of carriers in length L is q = nALe.
This moves through plane in wire in time t = L/vd.
Hence i = q/t = nAvde.
L
+
+
+
+
+
+
+

## Slide 4: Drift Speed, Resistance and Resistivity
Solve for vd to get:
In vector form:
Note, vd typically 10-3 m s-1!
Current through conductor related to potential difference across it through resistance, defined by:
Unit ohm (W = V A-1).
i = V/R, so increasing R reduces current: “resistance” aptly named!
Resistance is property of an object (a particular component in a circuit).
Resistivity, r, is property of material.
Defined by:
Units
In vector form,
Eqn.s for r only for isotropic materials.
Conductivity s is reciprocal of resistivity, conductance G reciprocal of resistance.
Units of s are S m-1, of G are S (S = Siemens or mho = W-1).
From above,

## Slide 5: Calculating Resistance from Resistivity
Calculate the resistance of a length L of wire of cross-sectional area A and resistivity r.
Assume E field and current density uniform throughout wire.
Hence E = V/L and J = i/A.
So we have
Resistivity varies with temperature, T.
For metals, the variation is fairly linear over a broad range of T.
Choose a reference temp. T0 at which the resistivity is r0.
(Usually T0 = 293 K, ~ room temp.)
Can then write:
The quantity a is the temperature coefficient of resistance.
For copper:
  r0 = 1.69 × 10-8 W m.
  a = 4.3 × 10-3 K-1.
L
i
i
V
A

## Slide 6: Ohm’s Law
current (A)
potential (V)
Contrast the behaviour of the current through two devices illustrated below:
For device “R”, the current is proportional to the voltage.
For device “D”, the current is small until V > 0.6 V at which point it increases sharply.
“R” obeys Ohm’s law, “D” does not.
Ohm’s law states: The current through a device is directly proportional to the potential difference applied to the device.
This holds for a resistance, as i = V/R with R the same for all V.
(Note that V = iR holds even for devices that do not obey Ohm’s law, where R is the resistance at that potential: devices obey Ohm’s law when the same value of R holds for all potential differences!)

## Slide 7: Conduction in Metals and Ohm’s Law
Charge transport in metals occurs as (some) electrons are free to move.
These have speeds of about 106 ms-1 and “bounce around” inside the metal, colliding with atoms on average every t seconds.
If an electric field is applied, the electrons experience a force F = eE and hence an acceleration
Between collisions they acquire a drift speed due to the E field of
Hence
But
As vd << 106 ms-1, t is approximately independent of E and therefore so is r.
Hence metals obey Ohm’s law.

## Slide 8: Power in Electric Circuits
Consider a device connected to a battery:
A charge dq passes through the device in a time dt with dq = i dt.
In passing through the device, the charge moves through a potential difference of V.
Hence, the potential energy decreases by dU = V dq = i dt V.
The power dissipated in the device (rate of energy transfer) is thus
Unit of power is the Watt (W = V A).
Combining with the expressions V = i R and i = V / R we get:
+
-
i
i
V

## Slide 9: Superconductors and Semiconductors
Superconductivity is observed in some materials, e.g. mercury.
For these materials, below a certain critical temperature (about 4 K for mercury), the resistance drops to zero.
Semiconductors, like silicon, have a resistivity that is between that of metals and insulators.
In metals, some of the “outer” electrons are only loosely bound and can be caused to move through the metal by the application of an E field.
In insulators all the electrons are tightly bound.
In semiconductors, some electrons can be freed by thermal energy.
Hence the resistivity of a semi-conductor is a strong function of its temperature.
Property | Copper | Silicon
Type of material | Metal | Semiconductor
Charge carrier density n (m-3) | 9 × 1028 | 9 × 1016
Resistivity r (Wm) | 2 × 10-8 | 3 × 103
Temp. Coeff. of resistance a (K-1) | +2 × 10-3 | -70 × 10-3