## Slide 1: Lecture 10
In this lecture we will look at:
  Electromotive force.
  Calculating the current in a circuit using the energy and potential methods.
  Internal resistance.
  Resistances in parallel.
  Resistances in multi –loop circuits.
After this lecture, you should be able to answer the following questions:
State Kirchoff’s voltage and current rules: what alternative names are used for these rules?
What is the current in a circuit in which resistors of 3 W and 5 W are connected in parallel with an emf of 9 V which has an internal resistance of 0.5 W?
Describe how the loop and junction rules can be used to determine the current in a circuit consisting of a network of resistors and emfs.

## Slide 2: Electromotive Force
In order to make charge carriers flow round a circuit, an “electromotive force” or emf is needed.
The job of a device providing an emf is to do work on the charges, pushing them through the resistance of the circuit.
Common emf devices are:
  Batteries.
  Solar cells.
  Generators.
All of these convert energy (chemical, light, mechanical) into electrical energy.
Consider circuit with emf E:
Within the emf, +ive charges move from low potential to high potential against the electric field.
The emf does an amount of work dW in moving a charge dq, define E as:
i
+ -
i
R
E

## Slide 3: Calculating the Current in a Circuit – Energy Method
Consider a simple loop circuit containing an ideal emf and a resistor, connected with wires of negligible resistance:
We know P = i2R, so in an interval dt, an amount of energy i2R dt will appear in the resistor.
During this time, a charge dq = i dt will have moved through the emf.
The emf will have done an amount of work dW = E dq = E i dt on the charge.
The work done by the emf must equal the energy appearing in the resistor.
Hence
Solving for the current:
i
+ -
i
R
E

## Slide 4: Current – Potential Method or Kirchoff’s Voltage Rule
Start at any point in the circuit and work round it, adding all the potential differences you come across.
Kirchoff’s voltage rule (or loop rule): The algebraic sum of the changes in potential encountered in a complete traversal of any loop of a circuit must be zero.
Start at –ive terminal of emf, which we assume has a potential V-.
Move to +ive terminal, potential difference is E.
Move along wires, no potential change as these have negligible resistance.
Move through the resistor, potential difference is –iR.
Move along wires, no potential change as these have negligible resistance.
Arrive back at point with potential V-.
From Kirchoff’s law:
i
i
R
+ -
E

## Slide 5: Internal Resistance
For our ideal emf:
Any real emf device has an internal resistance r, so
An ideal emf will always have a potential across its terminals equal to its nominal value (e.g. 12 V for an ideal 12 V battery).
A real emf will only have its nominal potential across its terminals when no current is flowing.
potential across external R
potential across internal r
+ -
E
r
E

## Slide 6: Resistance in More Complex Circuits
Add internal resistance:
Now get:
Add other resistances:
An identical current i flows through each resistance.
Hence
The combination of resistors can be replaced by an equivalent resistance
i
i
R
r
E
i
i
R2
R1
R3
+ -
E
i
i
Req
+ -
E

## Slide 7: Resistors in Parallel – Kirchoff’s Current Rule
Consider the following circuit:
We can see Kirchoff’s current rule (or junction rule) must apply: The sum of the currents entering any junction must be equal to the sum of the currents leaving the junction.
This tells us: i = i1 + i2 + i3.
We also know that: i1 = E/R1, i2 = E/R2 and i3 = E/R3.
Substituting these in the above:
The equivalent resistance for parallel resistors can then be found from:
i2 + i3
i
i
R3
+ -
E
R1
R2
i1
i2
i3
i2 + i3
i
i
Req
+ -
E

## Slide 8: Multi-loop Circuits
Consider the circuit:
Use loop rule LH loop:
Now for RH loop:
For outermost loop:
Now use junction rule at point a:
And at point b:
Now have 5 equations for 4 unknowns, solve for i1, i2, i3 and i4.
From (2)
From (4)
From (4) and (5) but also
From (1) and above:
R1
R3
R2
i2
i3
E
+
-
R4
i4
i1
a
b

## Slide 9: Multi-loop Circuits
Substituting for i3 and rearranging:
Strategy: use junction rule at every junction to give minimum number of unknown currents.
Apply loop rule around same number of different loops as there are unknown currents.
Solve equations for currents.
For some circuits there may be better (simpler) strategies...
E.g. here can find equivalent resistance due to R2 and R3 as these are in parallel:
Total equivalent resistance is then
Hence total current is