## Slide 1: Lecture 11
In this lecture we will look at:
  Measuring currents
  Measuring potentials.
  Circuits with resistance and capacitance.
After this lecture, you should be able to answer the following questions:
Explain why the resistance of an ammeter must be small and the resistance of a voltmeter large.
Write down the equation describing how the current in a series circuit containing a capacitance C, a resistance R, an emf E and a switch changes from the instant that the switch is closed.

## Slide 2: Measuring Current
The ammeter is used to measure current.
Must be inserted in the circuit (in series) at the point at which the current is to be measured.
The resistance of the ammeter, RA, must be small (RA << R + r ) otherwise the meter causes a change in the current.
Example, if R = 1 kW, r = 200 W, RA = 10 W and E = 12 V:
  i = 12/1200 = 10 mA before insertion of ammeter...
  ...and afterwards
i
+ -
E
R
A
i
R
RA
A
r
E

## Slide 3: Measuring Potential
The voltmeter is used to measure potential.
Must be connected across (in parallel with) the component over which the potential is to be measured.
The resistance of the voltmeter, RV, must be large (RV >> R + r ) otherwise the meter changes V.
Example, if R = 1 kW, r = 200 W, RV = 100 kW and E = 12 V:
Before insertion of voltmeter i = 10 mA, so V = 0.01 × 1000 = 10 V.
Afterwards the resistance seen by E is:
V
+ -
E
R
V
V
R
r
E
i
RV
V

## Slide 4: Measuring Potential
Hence new current:
The resistance over which the potential is measured is:
From these we obtain potential measured by voltmeter:
Numerically,
Note “potential divider”:
V
R
r
E
i
RV
V

## Slide 5: Circuits with Resistance and Capacitance
First consideration of circuits in which current varies with time: charging a capacitor.
Potential across capacitor VC(t) = q(t)/C.
Potential across resistor VR(t) = i(t) R.
Note these change with time!
Applying Kirchoff’s loop rule:
Cannot solve as contains two variables, i(t) and q(t).
However:
Hence,
Try solution:
Differentiating:
R
+ -
E
C

## Slide 6: Circuits with Resistance and Capacitance
Substitute into equation to check have solution.
The quantity t = RC is the time constant of the circuit: units seconds.
Using q = CV see solution can be written:
The differential w.r.t. time is the current through the circuit:
Check get expected limits:
  q(0) = 0.
  V(0) = 0.
  i(0) = E/R, (i.e. maximum current when switch first closed).
  q(∞) = CE.
  V(∞) = E.
  I(∞) = 0.

## Slide 7: Circuits with Resistance and Capacitance
Now think about discharging capacitor:
Using Kirchoff’s loop rule:
R
+ -
E
C
Try solution
Differentiating and substituting we get:
Voltage across C, current in circuit:

## Slide 8: Circuits with Resistance and Capacitance
Look at example:
  R = 1 kW, C = 1 mF so t = 1 ms.
  E = 10 V.
  Charge for 10 ms, then discharge:
If flip switch before charge “complete” (here at t = 2t):
volts
volts
amps
amps
secs
secs