## Slide 1: Lecture 20
In this lecture we will look at:
  Series LCR circuit.
  Resonance.
  Transients.
  Power in AC circuits.
After this lecture, you should be able to answer the following questions:
What is the impedance of a resistance R, an inductance L and a capacitance C connected in series?
Describe how the capacitive and inductive reactances change as the frequency of the sinusoidal signal driving a series LCR circuit increases from well below the circuit’s resonant frequency to well above it.
Explain the difference between the amplitude of an AC current and the rms value of the current. Why is the rms value a useful quantity?

## Slide 2: Series LCR Circuit
Have looked at AC circuits containing L, C and R separately.
What happens when all are present, connected in series?
Same current flows through all components.
Draw phasors for circuit, first current, i = I sin (wdt – f) :
Now phasors for vR, vC and vL, with the phase relationships: i same as vR; i leads vC by p/2; i lags vL by p/2.
E
vL
vC
vR
i
wdt – f
VR
VL
VC
vR
vC
vL
wdt – f
I
i

## Slide 3: Series LCR Circuit
Phasor for emf:
From the loop rule
Hence sum of phasors for vL, vC and vR must give phasor for emf:
Phasors for vL and vC have opposite directions, so mag. of sum is VL - VC.
From Pythagoras’ theorem,
Remember VR = I R, VC = I XC and VL = I XL, so:
Rearranging allows us to determine the amplitude of the current:
Here we have defined the impedance:
wdt
Em
E
VR
VL - VC
Em
wdt
f

## Slide 4: Series LCR Circuit
What about the relative phase of the current and the voltage?
Look again at the LCR phasor diagram:
We see
Now look at some LCR circuits.
All with Em = 325 V, f = 50 Hz:
R = 3W, C = 100 mF, L = 10 mH so XC = 0.032 W and XL = 3.14 W.
XL > XC, more inductive than capacitive, f +ive, i lags v.
VR
VL - VC
Em
wdt
f
(V)
(A)
(s)

## Slide 5: Series LCR Circuit
R = 3W, C = 1 mF, L = 0.1 mH so XC = 3.18 W and XL = 0.031 W.
XC > XL, more capacitive than inductive, f –ive, i leads v.
R = 3, C = 1 mF, L = 10 mH so XC = 3.18 W and XL = 3.14 W.
XL ≈ XC.
Notice current large and f ≈ 0.
(V)
(A)
(s)
0
0.02
0.04
0.06
400
200
0
200
400
200
0
200
E
t
(
)
i
t
(
)
t
(V)
(A)
(s)

## Slide 6: Series LCR Circuit: Resonance
Remember:
Resonance (maximum amplitude of current) when: XL = XC [20.4]
Recall also:
See tan f = 0, and hence f = 0, when XL = XC.
Can also change relationship between capacitive and inductive reactances by changing frequency at which circuit is driven.
Current amplitude given by:
Maximum when:
Recall natural frequency of LCR circuit is:

## Slide 7: Resonance and Phase
Plot current amplitude as function of r = wd/w, for R = 2, 0.5 and 0.2 W:
Maximum always when wd ≈ w, but sharpness of resonance changes.
Phase also changes as frequency varies:
Phase increases from –p/2, through zero as frequency passes through resonance, to +p/2.
I (A)
R = 2 W
R = 0.5 W
R = 0.1 W
R = 2 W
R = 0.5 W
R = 0.1 W
XC > XL
XL > XC
f

## Slide 8: Transients
Note, when the emf is first applied, it can take some time for the current to settle down to the steady state described by the equation i = I sin (wdt – f).
The additional current that flows initially is called the transient current.
The speed with which the transient current dies out is determined by the time constants of the circuit t = L/R and t = RC.
Example of behaviour that might be observed in LCR circuit at “start-up”:
(V)
(A)
(s)

## Slide 9: Power in AC Circuits
In LCR circuit energy is shifted between C and L (i.e. E and B fields) and lost to the circuit through the R.
If have emf, this replaces energy lost through R.
Power dissipated in R given by:
Mean rate of energy loss is this averaged over time.
From plot opposite, see average value of sin2 q, sin2 q = ½, so:
Plot of sin q and sin2 q:
Introducing the quantity Irms = I/√2 [20.7] we can write:

## Slide 10: Power in AC Circuits
Similarly define Vrms = V/√2 [20.9] and Erms = Em/√2 [20.10]
Remember we have:
We can divide through by √2 to get:
So we can write:
Using this we can recast the expression for the average power:
But, recall:
So
Hence
VR
VL - VC
Em
wdt
f