## Slide 1: CTA progress
Introduction
Imaging Atmospheric Cherenkov Telescopes
The CTA concept
CTA telescope designs
CHEC and the GCT
CTA and CTA-UK status
Summary
Notes: The Cherenkov Telescope Array (CTA) is the next generation observatory for ground-based gamma-ray astronomy. Current instruments (HESS, MAGIC and VERITAS) have made huge progress in the observation of cosmic sources of photons in the ~ 50 GeV to ~ 50 TeV energy range using Imaging Atmospheric Cherenkov Telescopes (IACTs). CTA will extend the range of these observations at both low and high energies, will improve their sensitivity by a factor of about 10 and will increase the precision of photon energy and direction measurements. This talk presents briefly the designs of the 23 m, 12 m and 4 m diameter IACTs that CTA will use to achieve this performance, before discussing the impact the array will have on studies of Fundamental and Astroparticle Physics. Topics covered include: searches for Dark Matter (DM) and axion-like particles (ALPs); studies of possible violation of Lorentz invariance; and studies of the sources and acceleration mechanisms of high energy cosmic rays.
Remember the Ellis/White paper.
Include EBL studies.

## Slide 2: Introduction
As of 28/8/2017, 08:00 (Irish Standard Time), 198 TeV g-ray sources known.
About half Galactic.
Majority found using Imaging Atmospheric Cherenkov Telescopes (HESS, MAGIC and VERITAS).
2

## Slide 3: Imaging Atmospheric Cherenkov Telescopes

e+
e-
VHE g causes EM shower with max. at alt. ~ 10 km.
Cherenkov angle ~ 1°: get ~ 10 ns light flash on ground with radius ~ 120 m.
Detect with camera made of PMs.
3
×
Primary g ray
~ 120 m
~ 10 km

## Slide 4: Current IACT arrays
VERITAS
HESS
4

## Slide 5: Current IACT arrays
MAGIC
5

## Slide 6: Supernova 1006
Distance 2200 pc.
Diameter of remnant about 20 pc.
First seen 1011 years ago:
Now seen in optical (yellow), X-ray (blue), radio (red)…
6

## Slide 7: Supernova 1006
…and in very high energy g-rays (HESS) :
Further progress in g-ray astronomy requires better sensitivity, energy and angular resolution – CTA.
Key CTA physics topics:
  Cosmic particles: how accelerated and propagated; impact on surroundings.
  Extreme environments: NS; BH; jets; winds; cosmic voids.
  Physics beyond the SM: what is DM; how distributed; do axion-like particles exist; UHE photons speed c?
CTA is an observatory: scientists in all contributing countries can apply for observing time.
7

## Slide 8: CTA performance goals
Aim for factor of 10 improvement in sensitivity.
Compare HESS ~ 500 hour image of galactic plane...
...with expectation with increased sensitivity, same exposure.
Expect to observe a few thousand sources (Galactic and extra-Galactic).
8

## Slide 9: CTA performance goals
Improve angular resolution by factor ~ 5.
Substructure of SNR shock fronts can then be resolved:
Better understand energy dependent morphology of pulsar wind nebulae.
HESS J 1825-137, size of emission region decreases with energy:
HESS resolution ~ 0.1°.
CTA resolution ~ 0.02 °.
9
> 2.5 TeV
1 – 2.5 TeV
< 1 TeV

## Slide 10: CTA performance goals
Increase field of view w.r.t. current instruments by factor ~ 2 to 4.5...9°.
Detect and map extended sources.
Improve survey capability: galactic plane at ~ 0.001 Crab in 250 hours, full sky at ~ 0.01 Crab in 1 year, ~ 300 times faster than current instruments.
Map source activity on sub-minute timescales.
Determine size of emission regions around active galactic nuclei.
Need fast slewing (20 secs), but also large FoV (Fermi g-ray burst monitor, has precision ~ 10°).
10

## Slide 11: Achieving CTA goals
Cherenkov emission, attenuation in air, QE of photomultiplier lead to:
  About 1 p.e./m2 in few ns for (frequent) 100 GeV g-ray.
  About 103 p.e./m2 in few 10 to 100 ns for (infreq.) 10 TeV g-ray.
Limitations:
  E < 100 GeV, Night Sky Background.
  E ~ 0.1...5 TeV, Cosmic Rays (need g/h sep).
  E > 5 TeV, rate.
Array of telescopes with different sizes copes best with these different regions.
11

## Slide 12: The CTA concept – southern array
Low energy
Four 23 m telescopes
4.5o FoV
~2000 pixels ~ 0.1o
Medium energy Twenty-five 12 m telescopes
8o FoV
~2000 pixels ~ 0.18o
High energy
Seventy 4 m telescopes
9o FoV
1000…2000 pixels ~ 0.17o…0.23o

## Slide 13: CTA performance
Sensitivity:
Performance dominated by Small Size Telescopes at energies above 5 TeV.
DE/E < 10% for Eg > 1 TeV.
Ang. Res. < 0.05° for E > 1 TeV.
13

## Slide 14: The LSTs
Dish 23 m diameter.
Focal length 28 m.
Mirror facets 1.5 m face-to-face.
Davies-Cotton design, modified to make isochronous.
Field of view 4.5°.
Camera diameter over 2 m.
Angular size of PMT pixels 0.1°.
Prototype under construction on La Palma (foundations completed).
Carbon fibre dish/camera support allows slewing to any point on sky in under 20 seconds.
14

## Slide 15: MSTs
Prototype structure near DESY-Zeuthen (Adlershof, Berlin).
Dish 12 m diameter.
Mirror facets 1.2 m face-to-face.
Camera diameter ~ 2 m.
Angular size of PMT pixels 0.18°.
FlashCam prototype:
15

## Slide 16: SCTs
Schwarzschild-Couder optics.
Primary diameter 9.7 m, secondary diameter 5.4 m.
Focal length 5.6 m (f = 0.58).
PSF better than 4.5’ across 8° field of view.
Angular pixel size 0.07°, 11328 SiPMs.
Prototype at Whipple Observatory, Arizona:
16

## Slide 17: SSTs
Three designs – two of which use Schwarzschild-Couder optics, third is Davies-Cotton.
Mirror diameter ~ 4 m.
Cameras all use SiPMs.
Field of view > 8 in all cases.
SST-1M, Krakow
ASTRI, Sicily
GCT, Meudon
17

## Slide 18: Status of the GCT
First light with CHEC-M in November 2015.
Prototype in March 2017:
GCT reaches any point on sky in 60 secs:
18

## Slide 19: Status of the GCT: structure
Excellent telescope balance ensures low power consumption:
Pointing precision:
Test of emergency stop:
Small amplitude oscillations of frequency ~ 1.5 Hz due to torsional movement of counterweight.
Addressed in design for pre-production GCT structure.
After
Before
Preliminary TPOINT correction
19

## Slide 20: GCT observing campaign March 2017
New power, safety and control systems.
Routine operation of GCT/CHEC-M.
Waveform of brightest pixel:
Thousands of Cherenkov images recorded, image analysis in CTApipe.
Integrated charge (p.e.) per pixel, fitted to extract Hillas parameters.
Peak signal arrival times (ns) per pixel.
20

## Slide 21: CHEC-S: architecture
21
32 modules, 8 × 8 pixels of size ~ 6 × 6 mm2
CHEC-S: silicon photomultipliers
(CHEC-M: multi-anode photomultipliers)

## Slide 22: CHEC-S: mechanical design
22

## Slide 23: CHEC-S: mechanical design
Rain and hail tests performed.
Focal plane cooling tested:
In Durham wind tunnel, opening and closing of doors functioned to 15 m/s.
Here at 12.5 m/s (CTA requirement):
With doors closed, survived max. wind speed of 30.7 m/s.
23

## Slide 24: CHEC-S: TARGET modules
24

## Slide 25: TARGET module performance
Pulse FWHM < 10 ns, dtpeak < 150 ps.
Gain spread TARGET module < 4%.
Max. cross talk < 0.7%.
Noise in module ~ 0.4 ADC counts.
CHEC-S SiPM + TARGET pulse-area spectrum:
Triggering:
Operation regime 3…4 mV/p.e.
Threshold 2.5 mV (0.6…0.8 p.e.),
Noise 0.44 mV (0.1…0.15 p.e.).
Threshold stable over large T range (1 mV change for 5 < T < 45 C).
Pedestal
1 p.e.
25

## Slide 26: Towards GCT design for pre-production
Based on knowledge gained during prototyping, final GCT telescope design optimized for pre-production.
Imminent launch of call for tender for GCT-01.
Contribute to array in Chile in 2019.
Pre-production camera very similar to CHEC-S.
Choice of SiPMs (with attendant modification of buffers) end 2017.
Install on telescope in Chile in 2019.
26

## Slide 27: Status of CTA
CTA timeline:
2016…17: hosting agreements signed, site preparation starts.
2019: deployment of first telescopes.
Funding level at ~ 65% of that required for baseline implementation.
  Start with threshold arrays (Paranal, 15 MSTs and 50 SSTs).
  Complete arrays as additional funding made available.
Construction takes ~ 6 years, initial science possible before construction end.
27

## Slide 28: Status of CTA consortium
MoU for construction, commissioning and operation of CTA discussed at most recent CTAC meeting in Rio de Janeiro (May 2017).
Propose are two membership classes:
Category 1)
  Contribute in a commensurate fashion to CTAC duties.
  Invest in the long-term one half or more of research time in CTAC.
  Have well defined contribution (hardware, software, analysis, infrastructure, management).
  Can opt-in to all CTAC publications.
Category 2)
  Do not satisfy above requirements, but bring identifiable benefit to CTAC.
  Can be invited to participate in individual CTAC publications.
Cat 1) members have free access to all CTAC data, software, tools, documents under control of CTAC.
Further discussion at next CTAC meeting in November on La Palma.
28

## Slide 29: CTAO progress
In Kind Contribution process.
Start from European Spallation Source example:
  Need to allow for many contributors from different shareholders (countries).
  Require coordinating institute for each IKC.
  Council wants relationship between CTAO and coordinating institute to be legally binding.
  Relationship between coordinating institute and other contributors MoU based?
For threshold array, allocate following contributions.
  North South 4 LSTs 15 MSTs 5 MSTs 50 SSTs
  Software blocks.
  Calibration instruments…
Later call(s) for baseline array, after all threshold components allocated:
  North South 10 MSTs 4 LSTs 10 MSTs 20 SSTs
29

## Slide 30: CTA southern site
Paranal, Chile.
Photo: Marc-Andre Besel
30
Aar, Namibia
Paranal, Chile
San Pedro Martir, Mexico
La Palma, Spain

## Slide 31: CTA site in Chile
31

## Slide 32: ESO Paranal site in Chile
32

## Slide 33: Summary
CTA will offer significantly increased sensitivity over current IACT arrays, coupled with improved energy and angular resolution.
CTA will allow investigation of a range of astrophysics and fundamental physics topics.
Plan to install first telescopes on southern and northern sites in 2019.
It’s time to plan how we intend to exploit this facility!
33