## Slide 1
Jon Lapington, CTA Consortium Meeting,
Turku, May 2015
GCT Camera Progress
Notes: STFC, Leicester, Oxford, Amsterdam, Wash U ST Louis, Adelaide
Liverpool, Durham, ?, SLAC, Santa Cruz, Hawaii

## Slide 2: GCT: The Gamma Cherenkov Telescope
Talks at this meeting:
  Monday SST
    SST configuration 3: GCT
  Tuesday SST
    GCT structure and optics
    GCT MC Studies
    Control of GCT camera peripherals
    GCT Camera Progress
    GCT Camera Software
    GCT Calibration
  Thursday Plenary
    SST-2M GCT progress report
    CHEC progress report
Notes: Monday: Tom Armstrong
Tuesday: Delphine Dumas, Tom Armstrong, Michael Daniel, me, Andrea de Franco, Anthony Brown
Thursday: Delphine Dumas, David Berge

## Slide 3: GCT: The Gamma Cherenkov Telescope
Contents:
Camera team evolution
CHEC-M
  Overview
  Mechanics
  Electronics
  Commissioning
  Auxiliary Systems
CHEC-S and beyond
  SiPMs
  Front-end electronics
Summary

## Slide 4: Evolution of the camera team
UK collaboration
  Leicester, Durham, Liverpool, Oxford, Liverpool John Moores (2015)
1st STFC funding 04/2012 – 03/2015, PI – Jim Hinton
March 2015: Jim, Rich, Akira  MPIK, Heidelberg
Proposed STFC funding 2015-2017, PI – Tim Greenshaw
Main camera development remains at Leicester
  Jon Lapington – lead (since 1st April 2015)
  Duncan Ross – mechanics
  Julian Thornhill – electronics
  Pippa Molyneux – commissioning
  External team
    Rich White, Akira Okumura, Arnim Balzer, Andrea De Franco, Jason Watson, Manuel Kraus, Tom Armstrong
Lab reorganization
  CHEC-M, CHEC-S, GCT assembly & commissioning

## Slide 5: CHEC-M in context
First GCT camera prototype
Properties:
  MAPMs
  TARGET 5 ASICs
To be installed on GATE later this year
The next step is CHEC-S
Properties:
  SiPMs
  TARGET 7 ASICs
 GCT pre-production camera
  SiPMs (LCT5, etc.)
  TARGET-C &TARGET-CCTV

## Slide 6: Overview
Lid motor
Motor Bulk-head Connectors
Lid Locking Mechanism
Photodetectors attached to trigger and digitisation electronics
Lid
Pointing LEDs
LED Flasher Units
Enclosure
Thermal Exchange Unit
Mounting eyelets
Focal plane plate
Desiccator
Telescope Interface
Power and data connections
Chiller send/return

## Slide 7: Overview
Windshield
DACQ boards
SFP (fibre) connection points
Backplane
Air-flow baffles
~0.5 m
Heat sink
Send / return to backplane cooling block
TARGET modules inserted into rack
Fans
Thermal Exchange Unit panel
Liquid-cooled block
Liquid send / return to chiller
Notes: From right hand side

## Slide 8: Overview
Pointing LEDs
Lid Locking mechanism
Cable inlet panel
Rack
Backplane
Peripherals Board
Air-flow baffles
Backplane cooling block
DACQ boards
Desiccator
Backplate
DACQ-to-Backplane cables
Mouting eyelets
Notes: From underside

## Slide 9: Overview
Cable inlet panel
Lid
Photodetectors
Connections to lid assembly
LED Flasher Units
Mounting eyelets
Lid motor
~0.5 m
~0.35 m
Notes: From front

## Slide 10: Electronics and Readout
x 32
Backend Electronics
Target Asic
FPGA
Target Asic
Target Asic
TARGET ASIC
16 x Preamps
16 x Preamps
16 x Preamps
16 x Preamp
64 Pixel Module
64 Pixel Module
TARGET Module
Trigger
Data
Any 2 neighbouring super-pixels
Following camera trigger data read out to central location
Control, & Data
Array/Clock Interface

## Slide 11: CHEC Back-End Electronics
Backplane
Photosensor, Preamp, TARGET Modules
IP addresses 1 - 8
DACQ Board 1
PC with 4 NIC
Photosensor, Preamp, TARGET Modules
IP addresses 8- 16
Photosensor, Preamp, TARGET Modules
IP addresses 16- 23
Photosensor, Preamp, TARGET Modules
IP addresses 24 32
Peripherals Board
SFP 1.1
SFP 1.2
DACQ Board 2
SFP 2.1
SFP 2.2
WR Switch
Camera Trigger and event number generation and distribution
Event numbers time stamped and sent to PC
Global Clock from DACQ
Peripherals (LED Flashers, Lid, Fans, Sensors ++
UDP TM Raw Data, Control / Monitoring
SPI Control / Monitoring
TM 4-pix Analogue Sum Trigger Signals
Camera Readout Trigger + Event #
TCP DACQ (and  SPI) Control / Monitoring
Notes: Update this if there is time
Trigger FPGA: 1760 pins, 256 mbit flash

## Slide 12: Electronics and Readout
Power and Monitoring PCB
ASIC and Readout PCB
House -Keeping FPGA
TARGET Module 1
Slow signal monitoring
Bias voltage trimming and pixel on/off
Shaping and amplification
64 Pixel Photodetector
TARGET Trigger ASIC
TARGET Trigger ASIC
TARGET Trigger ASIC
TARGET Trigger ASIC
TARGET Digitisation ASIC
TARGET Digitisation ASIC
TARGET Digitisation ASIC
TARGET Digitisation ASIC
Trigger FPGA
Photodetector Base PCB
Front-End Buffer
Timing Board
TARGET Module 32
Backplane
Lid motor
Lid lock motor
ALS
Limit switches
LED Flasher
Pointing LED
LED Flasher
Pointing LED
LED Flasher
Pointing LED
LED Flasher
Pointing LED
Motor controllers
Fans
Sensors
Focal Plane
Off-Camera
DACQ Board 1
DACQ Board 2
SFP
SFP
Peripherals Board
SFP
SFP
64 channels
Interface to focal-plane plate
FPGA
Flexible, shielded cables between buffer and TARGET module.
A single bias voltage is fed into all TARGET modules from outside the camera via the backplane and trimmed per SiPM tile
16 channels per ASIC
4 digital signals per ASIC, 16 per TARGET module
Slow raw data signals read out over SPI to FPGA
Control and monitoring using SPI and several GPIO
Fibre
18-way Ethernet switch
Connections from TARGET modules 1 – 16 input to DACQ1
Connections from TARGET modules 17 – 32 input to DACQ2
SFP
Full waveform digitisation
SPI
Temperature and humidity
Serial communications to set flasher pattern
PWM speed control
All TARGET I/O via copper connection
Raw analogue data
Raw digitised data
1 Gbps UDP over Ethernet link (copper or fibre) for raw data, control and monitoring
Discriminated analogue sum of 4-pixel digital trigger signals, 16 per TARGET module
Camera readout out and re-sync serial connection
Array-wide White Rabbit timing link input on 1 Gpbs fibre-optic link
1 PPS array-synchronous clock used to re-sync internal counters and sampling
62.5 MHz array-synchronous clock, multiplied to 125 MHz on the backplane
Asynchronous TTL pulse from the backplane to trigger the LED flashers
Internal serial communications for control and monitoring
Notes: Scheme for final GCT camera.
From sensor backwards, buffers, shielded cables, analogue functionality, 2 ASIC TM, Full BP and 2 DACQ boards with fibre to outside. Peripherals controls door, calib flashers and all housekeeping

## Slide 13: CHEC-M Camera Module
MAPM
(Hamamatsu H10966B)
High Voltage connection to the MAPM
Individual amplifier circuit
TARGET ASIC 16 channels digitisation and triggering
High Voltage supply
Mechanical standoff with retention for TARGET module to the backplane
Backplane connector carrying raw data, trigger and sync signals and power
Xilinx Spartan 6 FPGA (under)
Coaxial ribbon cables for analogue signals and preamplifier power
Front-end buffer module – 4 x 16 channel preamplifiers
PCB to interface with the focal plane plate

## Slide 14: CHEC-M Backplane
Trigger FPGA
(XC6VLX550T )
Notes: BP functionality:
Housekeeping FPGA
Trigger FPGA
Routes clock in, digital trigger out, serial comms in, digital raw data out
Trigger FPGA: 1760 pins, 256 mbit flash, >0.5M logic cells

## Slide 15: CHEC-M Backplane
Power Board connection
Trigger FPGA
Housekeeping FPGA pads
DACQ connections
Hardware complete – firmware under development

## Slide 16: CHEC-M Backplane
Lab tests proceeding with a proto-Backplane
All tests apart from triggering possible
Connection to DACQs
Trigger and CLK input & fan-out
Power to TARGET modules
Accommodates TARGET modules in identical way to real Backplane
PSU and switch box
Notes: Passive proto backplane plus tester board – no trigger functionality. TMs read out using tester board.

## Slide 17: CHEC-M DACQ Boards
Backplane connector
Differential clock
FPGA
ARM m-processor
SFP
University of Amsterdam & Seven Solutions:
  5 boards for manufactured, 2 iterations, both work, 2 for CHEC-M
2 boards provide:
  36 port switch
  4 x 1 Gb/s uplinks
  Absolute time synchronisation (using White Rabbit)
+12 V
RJ45 Debug
Notes: Add advantages of full waveform readout
Expand this slide:
-- Waveform
-- Photosensors
-- TARGET

## Slide 18: CHEC-M Calibration Units
Illumination of the focal plane via reflection from the secondary mirror
Installed in each corner of the camera
Performance:
  Multi-LED provides ~1 - 1000 pe
  Pulse width ~4 ns
1” diameter diffuser
M2
Camera focal plane
To M1
Diffused light from each corner of the camera
~0.5 m
Notes: Add advantages of full waveform readout
Expand this slide:
-- Waveform
-- Photosensors
-- TARGET

## Slide 19: CHEC-M Mechanics
Machined and bent Aluminum
Defocus of 1 mm  PSF degradation of 10% (on axis)
  Achieve ~0.35 mm spread between MAPM centres with no adjustment
  Can be reduced to 0.035 mm
Notes: Add advantages of full waveform readout
Expand this slide:
-- Waveform
-- Photosensors
-- TARGET

## Slide 20: Assembly
Internal rack built
Focal plane attached
Backplane and DACQ boards attached
TMs inserted

## Slide 21: Assembly
TMs pulled in from rear
  TARGET module inserted into slot in rack until screw mates with standoff
  TARGET module pulled into place with screw via tool inserted through backplane access hole
  TARGET module fully mated with backplane and secured in place
Pre-amps secured from front
MAPMs added
Enclosure added
ASIC and Readout PCB
Power and Monitoring PCB
Standoff
Backplane
Slot
Tool
Backplane Samtec connector
Threaded hole
TARGET module Samtec connector
Pre-amp retention washers

## Slide 22: Commissioning Lab Setup
Camera
Dark Box
Laser and diffuser
Camera mounted on sliding rail
Robot Arm
Initial setup for uniform illumination
Pulse Generator
Scope
Laser 12 V PSU
Control PC with TCP/IP control interface
Tester board
PC
Camera 12 V PSU
Tester board 12 V PSU
Proto. Backplane 5 V PSU
Control
Raw Data & Control
Trigger
Monitor SiPM
SiPM Out

## Slide 23: Commissioning Lab Setup
Light-tight enclosure (with roller blind)
Camera PSU and switch box
Notes: Add advantages of full waveform readout
Expand this slide:
-- Waveform
-- Photosensors
-- TARGET

## Slide 24: Commissioning Lab Setup
DACQ boards
proto-Backplane
Tester Board: FPGA board to generate CLK and Trigger signals for protoBackplane
Notes: Add advantages of full waveform readout
Expand this slide:
-- Waveform
-- Photosensors
-- TARGET

## Slide 25: Camera Readout
Raw data and slow control over 4 x 1 Gbps
Camera Server and Camera Controller software running as separate processes on 1 PC
Camera Server
  Listens for raw data, builds events, writes to disk (binary format stored in fits files, with protobuf headers)
  Receives run start / stop messages from Camera Controller
Camera Controller
  Reads in camera config (protobufs)
  Setups up the hardware (UDP raw socket to TM, zmq to DACQs)
  Signals run start / stop to Camera Server and sends run header
  Monitors camera (e.g. temperature) and writes to a fits file with time stamps
Offline
  Analysis chain, uses same protobuf structure for headers / config as online
  Assembles slow control and raw data based on timestamps
A lot of manpower has gone into this: libCHEC, see Andrea’s talk next…
Notes: Protocol buffers: language-neutral, platform-neutral, extensible mechanism for serializing structured data – like XML, but smaller, faster, and simpler
Zeromq: code connection in any language, on any platform

## Slide 26: Commissioning Progress
Laser flashes, externally triggered camera readout
Single pixel (289)
Pulse Area
Average over MAPM (module 8)
Pedestal subtracted, un-calibrated data
  Analysis chain and event-viewer under development
Notes: Pedestal-subtracted
Non-calibrated
Difference between ASICs visible
Gain spread within MAPM visible

## Slide 27: Auxiliary Systems
PSU
  Located behind M2
  Identical to the one being used in the lab
Chiller
  Cooling loop now tested in Leicester
GATE
Camera Power Supply
Chiller
Pipes
Dry / quick connections
Ethernet controllable
Camera Thermal Exchange Unit

## Slide 28: CHEC-S
See previous meetings for overview
Latest news:
  TARGET-7 modules under test at ECAP
  Last part of SiPM tile delivery delayed
  Front-end buffer and preamp now under test at Leicester with full SiPM tile attached to base
51.4 mm
51.4 mm
CHEC-S SiPM:
Hamamatsu S12642-1616PA-50
4 pixels combined to make 1 CHEC-S pixel
Through Silicon Via (TSV)
64 camera pixels
Depth of ~3.5 mm (including base PCB)
87% geometric fill factor
93% geometric fill factor possible with 6 mm pixels and same gaps, tile reduces to 50 mm x 50 mm
Micro coax cables
Rear of front-end buffer
Front of front-end buffer
Rear of SiPM base
Op-amps
Bias circuits
Latching connectors

## Slide 29: CHEC-S
Front end buffer tests
Only using mechanical samples thus far
Faster pulse rise time than previous devices
Ideal pulse requires more than p/z correction
SiPM tile, base and front-end buffer test in dark box
Preamp response with 1 pixel
Preamp response with 4 pixels

## Slide 30: CHEC-S
SiPM – epoxy coating requested
  Not supplied by Hamamatsu
  Thin (paralene?) coating only
  No waterproofing
Camera window required
Borofloat-33 glass
  Not obtainable thin enough
Shinkolite plastic
  Not obtainable thin enough
PMMA – Polycasa XT-UVT
  Thermal forming or blow moulding
  2mm thick82% trans.
  But high thermal expansion
  Need flexible seals
  Not obtainable thin enough

## Slide 31: Beyond CHEC-S
Conventional front-end electronics options
  CHEC-S discrete solution (integrated near sensor)
  Existing TARGET7 daughterboard design
PACTA chip – ICC-UB
  Multichannel ASIC front-end electronics
  Initially developed for LST/MST
  Designed for SiPMs (high capacitance)
  Integrated additional functionality for SST
TARGET-C and TARGET-CCTV
  Substrate noise  2 separate ASICs required
Latest SiPMs?
  Technology still improving
  No imp. from Hamamatsu after LCT5
  Other manufacturers still viable
  Larger pixel size
6 - 7 mm
200 mm gaps (50:50 dead:gap)
Gaps between tiles defined by tile tolerance (+_0.15 mm?)
50 - 57 mm?
Example of what we could specify
Final SiPM tile example
Hamamatsu (LCT5), Excelitas, SensL – all still viable

## Slide 32: Summary
CHEC-M commissioning in progress
Full testing limited by BP delay
  ..but delivery imminent
Meudon field trials
  Later in 2015
CHEC-S progressing
  First batch MPPCs delivered
  ..and will be attached to PCBs next
  Second MPPC batch due end-May