## Slide 1
May 2015
GCT Progress

## Slide 2: GCT: The Gamma Cherenkov Telescope
The UK-designed CHEC camera will equip the GCT
Optics and first mechanical design of telescope in UK
Prototype structure was assembled in Meudon (Paris Observatory) in April.
Prototype mirrors will be added in June.
Camera will be tested on telescope in September.

## Slide 3: Prototype telescope
Optical Support Structure and Alt-Az system

## Slide 4: Prototype telescope
Counterweight, mounting of Alt-Az structure

## Slide 5: Prototype telescope
Assembly completed in two days

## Slide 6: Camera Overview
Lid motor
Motor Bulk-head Connectors
Lid Locking Mechanism
Photodetectors attached to trigger and digitisation electronics
Lid
Pointing LEDs
LED Flasher Units
Enclosure
Thermal Exchange Unit
Mounting eyelets
Focal plane plate
Desiccator
Telescope Interface
Power and data connections
Chiller send/return

## Slide 7: Electronics and Readout
x 32
Backend Electronics
Target Asic
FPGA
Target Asic
Target Asic
TARGET ASIC
16 x Preamps
16 x Preamps
16 x Preamps
16 x Preamp
64 Pixel Module
64 Pixel Module
TARGET Module
Trigger
Data
Any 2 neighbouring super-pixels
Following camera trigger data read out to central location
Control, & Data
Array/Clock Interface

## Slide 8: CHEC-M Camera Module
MAPM
(Hamamatsu H10966B)
High Voltage connection to the MAPM
Individual amplifier circuit
TARGET ASIC 16 channels digitisation and triggering
High Voltage supply
Mechanical standoff with retention for TARGET module to the backplane
Backplane connector carrying raw data, trigger and sync signals and power
Xilinx Spartan 6 FPGA (under)
Coaxial ribbon cables for analogue signals and preamplifier power
Front-end buffer module – 4 x 16 channel preamplifiers
PCB to interface with the focal plane plate

## Slide 9: Assembly
Internal rack built
Focal plane attached
Backplane and DACQ boards attached
TARGET Modules inserted

## Slide 10: Assembly
TMs pulled in from rear with screw via tool inserted through backplane access hole
Pre-amps secured from front
MAPMs added
Enclosure added
ASIC and Readout PCB
Power and Monitoring PCB
Standoff
Backplane
Slot
Tool
Backplane Samtec connector
Threaded hole
TARGET module Samtec connector
Pre-amp retention washers

## Slide 11: Commissioning Lab Setup
Camera
Dark Box
Laser and diffuser
Camera mounted on sliding rail
Robot Arm
Initial setup for uniform illumination
Pulse Generator
Scope
Laser 12 V PSU
Control PC with TCP/IP control interface
Tester board
PC
Camera 12 V PSU
Tester board 12 V PSU
Proto. Backplane 5 V PSU
Control
Raw Data & Control
Trigger
Monitor SiPM
SiPM Out

## Slide 12: Commissioning Lab Setup
Light-tight enclosure (with roller blind)
Camera PSU and switch box

## Slide 13: Commissioning Lab Setup
DACQ boards
proto-Backplane
Tester Board: FPGA board to generate CLK and Trigger signals for protoBackplane

## Slide 14: CHEC-M Commissioning Results
Laser flashes, externally triggered camera readout
  Full libCHEC software setup: camera server, controller “online”
  “offline” data analysis
  Use waveform sampling: per event, step through waveform around peak
  Fake air-shower images with mask

## Slide 15: CHEC-S
Latest news:
  TARGET-7 modules under test in Erlangen
  Front-end buffer and preamp now under test at Leicester with full SiPM tile attached to base
51.4 mm
51.4 mm
CHEC-S SiPM:
Hamamatsu S12642-1616PA-50
4 pixels combined to make 1 CHEC-S pixel
Through Silicon Via (TSV)
64 camera pixels
Depth of ~3.5 mm (including base PCB)
87% geometric fill factor
93% geometric fill factor possible with 6 mm pixels and same gaps, tile reduces to 50 mm x 50 mm
Micro coax cables
Rear of front-end buffer
Front of front-end buffer
Rear of SiPM base
Op-amps
Bias circuits
Latching connectors

## Slide 16: CHEC-S
Front end buffer tests
Only using mechanical samples thus far
Faster pulse rise time than previous devices
SiPM tile, base and front-end buffer test in dark box
Preamp response with 1 pixel
Preamp response with 4 pixels

## Slide 17: Summary
Prototype GCT assembled
Mirrors under construction and test
  On telescope in July
CHEC-M commissioning in progress
Meudon field trials
  Later in 2015
CHEC-S progressing
  First batch of MPPCs delivered
  Second MPPC batch due end-May