## Slide 1: The Gamma-ray Cherenkov Telescope
Pre-history, theory and experiment.
CTA and the SSTs.
GCT optical design.
GCT mechanics.
Camera.
First Cherenkov light.
Some things we have already learnt?
What next?
Summary.

## Slide 2: Schwarzschild-Couder telescopes
sF
KF
In 2002, Lynden-Bell described all spherical aberration and coma free dual mirror telescopes, in terms of:
  s × F – mirror separation.
  K × F – secondary to focus.
In 1905, Schwarzschild described a telescope with two concave mirrors and the focal plane between the mirrors.
He showed this suffered no spherical aberration or coma, but significant astigmatism, partly as focal surface assumed flat.
Couder (Paris Observatory) modified this design in 1926, allowing the focal surface to be curved and curing (some of) the astigmatism.
Figured mirrors in 1930s, but telescope never built (because 6 m long for primary diameter D = 0.8 m and focal length F = 2.4 m?).
2

## Slide 3: Cherenkov light from air showers
The first detection of Cherenkov light from air showers was made in 1953:
Seen by Galbraith and Jelley using a parabolic mirror viewed by a phototube.
An early “dual mirror” gamma ray telescope, Porter and Jelley, Glencullen (Ireland), 1962.
Gun mount and searchlight mirrors from WWII.
3

## Slide 4: The first TeV source…
4
Whipple, completed 1968

## Slide 5: Imaging Atmospheric Cherenkov Telescope arrays
VERITAS
HESS
5

## Slide 6: Imaging Atmospheric Cherenkov Telescope arrays
MAGIC
6

## Slide 7: The Cherenkov Telescope Array
Low energy
Four 23 m telescopes
4…5o FoV
~2000 pixels ~ 0.1o
Medium energy
About twenty-five 12 m telescopes
6…8o FoV
~2000 pixels ~ 0.18o
High energy
About seventy 4 m telescopes
8…10o FoV
1000…2000 pixels ~ 0.17o…0.23o

## Slide 8: The SSTs – take one
Davies-Cotton 7 m telescope designed for CTA.
This is a viable solution for the SST.
But, the camera:
  Has a diameter of about 1.6 m.
  Weighs about 2 tonnes.
  Is expensive, in no small part because of the price of the PMTs.
The cost of the camera dominates that of the telescope.
Making it cheaper would allow the construction of more telescopes and hence improve CTA performance.
8

## Slide 9: The SSTs – take two
Can we use cheaper sensors (e.g. SiPMs) in a compact camera?
Must have F ~ 2 m so ~ 6 × 6 mm2 pixels commercially available match required angular resolution of ~ 0.2°.
Need reasonable area, D > 3 m, hence “fast” focal ratio (f = F/D small).
Primary aberrations:
  Spherical ~ 1/f3.
  Coma (1st order) ~ d/f2.
Require sophisticated optics to correct for aberrations at large field angles.
Look at two-mirror telescope designs, proposed by Vassiliev for AGIS.
9

## Slide 10: Telescope optics
Scan (s, K) space: “best” telescope has s = 1.56, K = 0.224, F = 2.28 m.
D1 = 4 m, D2 = 2 m, f = 0.57.
Focal surface spherical, r = 1 m.
Numerical optimisation using ZEMAX.
Sacrifice on-axis PSF for improved performance at large field angles.
D80 (m)
d (°)
Exact Optics
ZEMAX
10
3.56 m
0.51 m

## Slide 11: Telescope optics
ZEMAX design:
Images of point source at infinity:
For field angles below about 5, over 80% of the light from a point source at infinity (or at 10 km with refocusing) is contained in a 6 × 6 mm2 pixel.
11
d = 0°
d = 4°

## Slide 12: Mechanical design
Durham 2011.
Long fork.
Central tube supports camera.
Tripod supports secondary mirror
Electronics in counterweight.
Aluminium structure.
Paris, 2012.
Short fork.
Primary dish support separated from secondary support.
Camera attached to secondary.
Shaped counterweight.
Steel structure, aluminium mirrors.
12

## Slide 13: Mechanical design
Paris 2015.
Four masts to support secondary.
Same motors on both axes.
Primary mirror rotation mechanism to facilitate mirror installation.
Camera removal mechanism.
13

## Slide 14: Mechanical structure
Structure assembled in Meudon in April, visited by ESO team in September.
14

## Slide 15: Dual Mirror – alternative Italian design
Camera
Mast structure
Counterweight
Primary mirror with sector panels
Concrete pedestal and foundation
Secondary mirror
Worm drive
M1 dish
Elevation universal joint
(Cardan joint)
15

## Slide 16: Dual Mirror – alternative Italian design
Elevation 90°
Elevation 30°
Azimuth 180°
Elevation 30°
Azimuth 0°
Elevation 30°
Azimuth 90°
Elevation 30°
Azimuth –90°
Illustration of functioning of Cardan joint and worm drives.
Give access to:
  Elevation 30...90°.
  Azimuth –180...180°.
16

## Slide 17: ASTRI – prototype design
Base
M1 dish
M1 active surface
M2 Back-Up Structure
Mast
EL actuator
AZ fork
EL axis
Electrical cabinets
M2
M1 electrical boxes
Snow shields
Counterweight

## Slide 18: Camera design
Target Asic
FPGA
Backplane
Target Asic
Target Asic
TARGET ASIC
16 x Preamps
16 x Preamps
16 x Preamps
16 x Preamp
Timing Board
64 Pixel Module
Backplane Board
64 Pixel Module
TARGET Module
Peripherals (calibration, lid, etc)
Trigger
UDP Data
x 32
Amplification and shaping
Digitisation and Trigger
Buffering and Serialisation
Camera Trigger
DACQ Boards
Safety Boards
Clock, Timestamps
Data
Goal – produce low cost camera
with full-waveform readout
18

## Slide 19: Development of the camera
Leicester 2012, start construction of camera with MAPMs – CHEC-M.
Electronics based around TARGET (Hawaii/SLAC and Erlangen).
DAQ using White Rabbit for timing (Amsterdam).
Backplane, common with SCT (Washington University).
Flashers (Durham) and Peripherals Board (Liverpool) complete camera.
19

## Slide 20: Development of the camera
Leicester 2015, CHEC-M complete.
Lid motor
Motor Bulk-head Connectors
Lid Locking Mechanism
Photodetectors and front end electronics
Lid
Pointing LEDs
LED Flasher Units
Enclosure
Thermal Exchange Unit
Mounting eyelets
Focal plane plate
Desiccator
20

## Slide 21: Completing the GCT prototype
Camera mounted on telescope on Friday 20th November…

## Slide 22: Verify camera operation on telescope
Check that operation safe, e.g. TARGET module temperatures.
Check electronics performance, e.g. transfer functions.
Check that MAPMs functioning as expected – look for single photo-electron peak:
222

## Slide 23: First tests of the GCT prototype on sky
Thursday 26th Nov, night sky background 20 to 100 times higher than CTA sites…

## Slide 24: First tests of the GCT prototype on sky
…but successfully observed Cherenkov light from ~ 50 TeV showers.
24

## Slide 25: First tests of the GCT prototype on sky
25
Thursday 26th November.

## Slide 26: First tests of the GCT prototype on sky
26
Thursday 26th November.

## Slide 27: First tests of the GCT prototype on sky
27
Thursday 26th November.

## Slide 28: What have we learnt?
All the stuff you have heard in the telescope and camera talks, plus..
Time invested in simplifying installation/maintenance procedures is time well spent – need handles on camera!
Prototype helps identify problems you wouldn’t otherwise spot.
E.g. need for “dummy connectors” to which tubes and cables can be attached when the camera is not on the telescope – prevents things flapping around and keeps them clean.
Prototype aids production and checking documentation.
288

## Slide 29: What have we learnt?
We need to work on mirrors and mirror production processes.
Can see by eye that two panels of the secondary are of poor quality (despite nominally all being same).
Try casting aluminium, machining, applying nickel layer, polishing, coating with aluminium and SiO2.
Nickel layer improves surface quality, but also needed if mirror to be recoated, otherwise old Al coating cannot be stripped off.
Good quality control needed.
Casting should also reduce cost.
(Applies also to structural elements.)
Bad panel in GCT secondary.
299

## Slide 30: First glass mirror studies
Hot slump glass mirrors using concave mould.
Proof-of-principle studies.
Grind a ceramic mould with radius of curvature of 3 m.
Level mould in oven and slump 4 mm thick glass sheet, 35 cm diameter, using carefully controlled temperature cycle.
30

## Slide 31: First glass mirror studies
Chart: 
| Run1 | Run 2 | Run 3 | Run 4 | Average
Mould pre bake | 2993.4 | 2993.5 | 2993.5 | 2993.7 | 2993.4
Mould post bake | 2999.67 | 2999.52 | 2999.85 | 3000.19 | 2999.67
Part 1 | 3006.41 | 3005.97 | 3006 | 3006.55 | 3006.41
Part 2 | 2969.54 | 2969.94 | 2968.89 | 2969.73 | 2969.54
Measure RoC of glass samples and mould.
Mould relaxes slightly after baking.
Part 1, slumped simultaneously with mould baking, during power cut.
Part 2, smaller RoC than mould as expected.
Glass follows shape of mould.
Deviations about ± 25 nm.
Next steps, larger samples, petal shapes, smaller RoC, coating…
31

## Slide 32: Further glass mirror studies
Tender put out for GCT mirror panels (thanks to MPI and Andreas Foerster!).
Specifications included table of required mirror surface quality:
Flabeg cannot meet “waviness” criteria: 20 mm (M1) 50 mm (M2).
Need to clarify this: parameters understood? What is the ASTRI experience?
Flabeg suggest using thinner glass is possible approach.
Another reason for working on mirrors is cost…
332

## Slide 33: Immediate next steps
GCT
  Complete commissioning and testing of GCT camera and structure.
  Put together Expressions of Interest for Project Office that cover construction of 35 GCTs.
  Design pre-production camera and telescope.
  Review design.
  Get more money!
SST
  Need foundation suitable for all SSTs (for TDR update?).
  Common actuators (ditto?).
CTA
  Site and information on site.
  Agreement on common control systems (e.g. PLCs) would be good (tied with site negotiations?) to reduce amount of effort invested in this area.
33

## Slide 34: Summary
Thanks for coming to the party!