## Slide 1: SOLAR ENERGY
The average solar power incident on earth is ~ 1kW m-2 or 105TW
Current world power needed is
~15 TW, ~ 11% from biomass
and ~85% from fossil fuels, both
of which are a consequence of
photosynthesis.
Photovoltaic cells have an
efficiency ~ 15% cf ~ 0.2 - 2% for biomass
AM0 = 1.36 kW m-2 is the intensity on the atmosphere which is reduced to AM1.5 = 1 kW m-2 incident on the surface at 48o to the vertical
Absorption in the atmosphere is mainly below photon energies
<~ 1.7 eV in the infrared
Typically ~ 30% of sunlight is diffuse
Variations in intensity depending on location and cloud cover

## Slide 2: P-N JUNCTION CHARACTERISTICS
A p-n junction is manufactured by doping a silicon wafer
The resulting energy diagram shows how the device is non linear with forward and
reverse characteristics
depending on the polarity
of the applied voltage
When unbiased there is
~0.6V across the depletion
region
The forward current in a p-n
junction is given by
I = IS{exp(V/VT)-1} (10.1)
IS is the saturation current and
VT  kT/ e ≈ 0.026V
at room temperature
Ideal diode Actual behaviour

## Slide 3: SOLAR PHOTOCELLS
A photocell is basically an unbiased p-n junction exposed to light
Photons can be absorbed by the photoelectric effect in which an electron absorbs the photon’s energy and creates an electron – hole pair
  Need photons with energy > band gap energy Egap, >1.1 eV in silicon corresponding to a wavelength of ~1.1 mm
The built in field in the depletion region sweeps electrons to the n-side and holes to the p-side creating a reverse current IL
The photocell current IC is given by
IC = IL - IS{exp(V/VT)-1} = IL - IS{exp(ICR/VT)-1} (10.2)
where IC creates the forward bias V = ICR where
R is the resistive load on the photocell
        R
This forward bias gives rise to the second term (10.2) in the opposite direction to the light induced current IL

## Slide 4
A cell consists of a p-n junction with metal electrodes
  The top electrode is in narrow strips to allow illumination
A highly doped n+ layer
reduces the series resistance.
A highly doped p+ layer
minimizes surface
recombination at the rear contact by reducing the electron
concentration in this region.
An anti-reflective coating is included
When R=∞ , IC = 0 and the open circuit voltage is given by
VOC= VT ln(1 + IL/IS) ≈ VT ln( IL/IS ) since IL>>IS (10.3)
When R = 0, V=0 and the short circuit current ISC = IL
For a finite resistance R, IC generates power
PC = IC V = IC 2R (10.4)

## Slide 5
The maximum voltage VOC must be less than the band gap
As V increases PC increases until V is
slightly less than VOC
If ISC = 1 mA (= IL ) & IS= 10-14 A then
(10.3)  VOC =0.66V
From (10.2) & (10.4) we can calculate
IC for a given V and then PC as shown
At the maximum power point Pm = 0.55 mW, Vm = 0.58V and Im = 0.95 mA . Note that Im & Vm are close to ISC and VOC
The fill factor is defined as FF = Pm /(ISCVOC) (10.5)
FF is useful for quality control, typically in range 0.75 – 0.85
V (V) | 0.10 | 0.30 | 0.50 | 0.55 | 0.58 | 0.60 | 0.62 | 0.64 | 0.66
I (mA) | 1.0 | 1.0 | 1.0 | 0.98 | 0.95 | 0.89 | 0.77 | 0.51 | 0.0
P (mW) | 0.1 | 0.3 | 0.5 | 0.54 | 0.55 | 0.53 | 0.48 | 0.33 | 0.0

## Slide 6: EXAMPLE:- A photocell has IS=2 10-12 A, ISC = 30 mA and an area of 1cm2. Find Pm, FF and the conversion efficiency of the cell. What resistance is required across the cell to give maximum output?
From (10.3) using VT = 0.026V and IL≈ ISC we get VOC = 0.61 V
Calculating I from (10.2) and P from (10.4) produces the table
Peak power Pm = 15.2mW when Vm = 0.53V and Im = 28.6 mA
From (10.5) FF = Pm / ISCVOC = 0.0152 / (0.030 x 0.61) or 83%
Approximately 100 mW cm-2 of solar radiation falls on this cell so
its efficiency is ~ 15%
The resistance for maximum output is
R = Vm / Im = 0.53 / 0.286 = 18.5W
V (V) | 0.5 | 0.52 | 0.53 | 0.54 | 0.56
I (mA) | 29.6 | 29.0 | 28.6 | 27.9 | 25.5
P (mW) | 14.8 | 15.1 | 15.2 | 15.1 | 14.3

## Slide 7: EFFICIENCY OF SOLAR CELLS
Conversion efficiency is defined as the ratio of Pm to incident solar power AM1.5 close to 100 mW cm-2
Factors effecting efficiency are:-
23% of photons have E < 1.1 eV
Only 1.1 eV of the energy of any
higher energy photons is required
to produce power so only 47% of
the incident energy contributes to
the power with 30% going to heat.
Hence 47% is the limiting value of efficiency for a solar cell
Of course the 1.1 eV simply produces the electron-hole pair while the useful power produced is | e | Vm . The ratio
| e | Vm / Egap ~ 0.65 which is another significant reduction
Finally ~10% of the electron-hole pairs recombine before collection

## Slide 8
Reflection is potentially a 40% loss but this is reduced by an anti-reflection coating of ¼ wavelength material
Reflection coefficient from silicon without
a coating is r = (n0-n2)2 / (n0+n2)2
Silicon refractive index averages to ~ 3.5
so r ~ 40%
Introducing a ¼ l coating with refractive
index n1 given by n12 = n0 n2 reduces the value to r ~ 6% and multiple
coatings can reduce this to 1% and other small losses amount to ~3%
Multiplying these factors hC ≈ 0.47 x 0.65 x 0.9 x 0.96 ≈ 26%
Decreasing Egap increases the photocurrent (reduces 23% factor) but decreases Vm since |e |VOC < Egap
  The optimum value is Egap =1.4 eV
  GaAs and CdTe have band gaps close to this

## Slide 9
Dependence of the short circuit
current density jSC on Egap is shown
Approximately
jSC ≈ A – B Vg mA cm-2 (10.6)
A = 80 mA cm-2, B = 34 mA V-1
and Vg = Egap / |e |
Also VOC ≈ Vg – 0.46 V (10.7)
(Details in derivation 6.2 in text book)
Max. power Pm ≈ FF(A – B Vg )(Vg – 0.46 ) mW cm-2 (10.8)
Assuming the fill factor stays constant this has a maximum when Vg = A/(2B) +0.23 ≈ 1.4 V
For a silicon cell with Egap = 1.1eV and FF = 0.8
then (10.8) gives Pm ~ 25 mA cm-2
The following table gives examples for different types of cell

## Slide 10
sc - single crystal
mc – multicrystalline
single – single junction
multi – multiple junctions
 |  | Efficiency % for cell area | 
Material | Band gap eV | ~ 1 cm2 | ~ 1 m2
GaAs | 1.4 | ~24 | 
GaAs (multi) | 1.8 – 0.7 | ~34 | 
Si (sc) | 1.1 | ~24 | 
Si (mc) | 1.1 | ~20 | ~13
a-Si(single) | ~1.7 | ~12 | ~7
a-Si(multi) | ~1.7 – 1.3 | ~13 | ~10
CdTe | 1.5 | ~16 | ~8
CuIn1-xGaxSe2 | ~1.2 | ~19 | ~12

## Slide 11: EXAMPLE:- A 4cm2 GaAs solar cell has IS = 4 10-15 mA. ISC = 127 mA under AM1.5 solar radiation. What is the conversion efficiency under normal and 100 x normal illumination? (Assume IL ≈ ISC)
From (10.3) VOC = VT ln(ISC / IS ) = 0.026 ln(127/ 4 10-15)
VOC = 0.988V
Need to obtain approximations for the Vm and Im. Start by maximising P = I V where I is given by (10.2)
IC = IL - IS{exp(V/VT)-1} so P = V[IL - IS{exp(V/VT)-1}]
Max. power when dP/dV =0
So [IL - IS{exp(V/VT)-1}]-(V/VT) ISexp(V/VT)=0
(1 + V/VT) exp(V/VT) = (IL / IS + 1) or approximately
(VOC/VT) exp(Vm/VT) = IL / IS= exp(VOC/VT) (10.9)
Taking logs ln(VOC/VT) + Vm/VT = VOC/VT
Writing xOC = VT/VOC we get Vm =VOC{1+ xOC ln(xOC)} (10.10)

## Slide 12
Then from (10.2) Im = IL - IS{exp(Vm/VT)-1} and IL ≈ ISC
Using (10.9) Im = ISC - IS{ (IL / IS)(VT/VOC)-1} ≈ ISC (1- VT/VOC)
Im ≈ ISC ( 1 – xOC) (10.10)
FF = Pm / ISCVOC = {1+ xOC ln(xOC)} ( 1 – xOC) (10.11)
VT ~ 0.026V so xOC = 0.0263 leading to
Vm = 0.988{1+0.0263 x ln(0.0263)} = 0.89 V
Im = 127(1 – 0.0263) = 124 mA
Pm = 0.89 x 124 = 110 mW
Under 100 x illumination VOC increases as ISC is 100x larger
VOC = 0.026 ln(12700/ 4 1015) = 1.108 V and new values:-
xOC = 0.0235, Vm = 1.01 V, Im = 12.4A , Pm= 12.5W
At Am1.5 the solar power on the cell = 4 x 100 mW = 400 mW
Conversion efficiency = 110 / 400 = 28%
At x100 illumination the ratio is 12.5 / 40 = 31% ( 10% increase)