## Slide 1: NEUTRONS AND THEIR INTERACTIONS
Discovered by Chadwick in 1932 from reaction
9Be5 + a  12C6 + n + 5.75 MeV (Q value)
Neutrons do not occur as free particles as they undergo b decay
T1/2 = 10.6 min
Neutrons can be produced using a mixture of radium and beryllium
236Ra  232Rn + a then a + 9Be 12C + n
1g of Ra + few g of Be produces ~ 107 neutrons / s
INTERACTIONS OF NEUTRONS
Neutrons are uncharged so do not experience Coulomb repulsion.
  Can interact with nuclei at thermal energies with kT ~ 1/40 eV
Interacting at low energies is important since
s(low energy) >> s(high energy)
There are two principle modes of interaction between neutrons and nuclei

## Slide 2
ELASTIC SCATTERING sS
This is an important mechanism for slowing down neutrons --- MODERATION
The initial energy goes into the recoil energy of X + slower neutrons
COMPOUND NUCLEUS FORMATION
A neutron is absorbed by the target nucleus leaving the ‘compound nucleus’ in an excited state
After formation of the compound nucleus several things can happen
a) INELASTIC SCATTERING si

## Slide 3
b) RADIATIVE CAPTURE sc
EMISSION OF LIGHT CHARGED PARTICLES sR
d) FISSION sF
TOTAL CROSS SECTION sT = si + sC + sR + sF + sS (16.1)
ABSORPTION CROSS SECTION (neutrons removed from flux)
sA = sC + sR + sF (16.2)
All ss depend on the neutron’s kinetic energy
sR is usually small and we will ignore it

## Slide 4
The plots below sketch the behaviour of the neutron capture cross section
in 238U and the neutron induced fission cross section in 235U

## Slide 5
FISSION
Q = [M(A,Z) – M(A1,Z1) - M(A2,Z2) ] c2
Energetically favoured since d(A/2) > d(A)
Spherical shape gives lowest energy configuration ( LIQUID DROP)
Energy is required to deform the nucleus increasing the surface
area until Coulomb forces can complete the split
The extra energy needed to do this is called the
FISSION BARRIER or ACTIVATION ENERGY Ef

## Slide 6: SPONTANEOUS FISSION
Consider the possible fission of 23892U into 2 identical nuclei 11946Pd
For uranium & palladium d ~ 7.6 MeV & ~8.5 MeV / nucleon
 Q ~-238 x 7.6 – (-2 x119 x 8.5) = 214 MeV
Is this a possible decay mode?
The diagram has zero potential
corresponding to the final state.
As in alpha decay the Coulomb
Barrier (height EC) prevents
immediate decay since Q < EC(~250 MeV)
It is necessary to supply energy to deform the nucleus which increases the
dominant surface energy term while initially reducing the Coulomb term.
Hence a strong restoring force initially prevents fission until at a certain
separation the relative strengths reverse as the charges separate further and
fission occurs.

## Slide 7: NEUTRON INDUCED FISSION
In this case the compound nucleus
is formed in an excited state as the
absorbed neutron has contributed
its binding energy |Bn |
Consider 23692U formed as a compound nucleus by the capture of a slow neutron by 23592U
M(235U) = 235.043933 u & M(n) = 1.008665 u so
Sum = 236.052598 u compared with M(236U) = 236.045733 u
DM = + 0.006865 u  + 6.5 MeV
236U is formed excited with energy Ex = |Bn | = 6.5 MeV
For 236U Ef = 5.9 MeV
Ex > Ef so fission is possible with thermal neutrons in this case (K.E. of neutrons Tn ~ 1/40 eV)

## Slide 8
In general if | Bn | < Ef then neutrons require Kinetic Energy Tn to induce fission
i.e. Tn + |Bn | > Ef
e.g. 238U for example where Tn > 1 MeV is required
The difference between the two compound nuclei is because of nucleon pairing energy
|Bn even-even | > |Bn even-odd |
So |Bn 236U | > |Bn 239U | and neutron K.E. is required to fission 239U
SPONTANEOUS FISSION occurs with small probability by tunnelling through the barrier
e.g. For 238U in the absence of a decay
T1/2 ~ 1015 years

## Slide 9: Example: Calculate the fission thresholds for the reactions 1) n + 232Th233Th*fission and 2) n + 239Pu240Pu*fission
Masses : 232Th (232.038050 u) 233Th (233.041577 u)
239Pu (239.052157 u) 240Pu (240.053807 u)
n (1.008665 u)
1) Excitation for 233Th is = (232.038050 + 1.008665 - 233.041577)
= 5.138 10-3 u  4.8 MeV
Activation energy Ef = 6.7 MeV so threshold energy = 1.9 MeV
2) Excitation for 240Pu is = (239.052157+1.008665- 240.053807)
= 7.02 10-3 u  6.53 MeV
Activation energy Ef = 6.3 MeV so there is no threshold energy

## Slide 10
FISSION BARRIERS AND NEUTRON BINDING ENERGIES
REACTION NEUTRON + | COMPOUND NUCLEUS | Ef MeV | Bn MeV | Tn MeV FOR FISSION
232Th | 233Th* | 6.7 | 4.8 | ~ 1.9
233U | 234U* | 5.85 | 6.8 | 0
235U | 236U* | 5.9 | 6.5 | 0
238U | 239U* | 5.8 | 4.8 | ~ 1.0
239Pu | 240Pu* | 6.3 | 6.5 | 0
Only for Z >90 is Ef small enough for low energy neutrons to induce fission
The important naturally occurring fissionable nuclei
are 232Th, 235U (0.7% natural U) ,and 238U (99.3% natural U)
For A>250 Ef 0 and spontaneous fission becomes a probable decay mode
TABLE 1

## Slide 11
ENERGY RELEASE
Approximately 200 MeV is released in fission of a heavy nucleus :
MeV
K.E. of fission fragments 165 ± 5
Prompt g-ray energy 7 ± 1
K.E. of fission neutrons 5 ± 0.5
– rays from fission products 7 ± 1
g– rays from fission products 6 ± 1
Neutrinos from fission products 10 TOTAL ~ 200
MASS DISTRIBUTION OF FISSION FRAGMENTS
In low energy fission processes there is a
wide distribution of nuclear masses
Produced, with equal fragmentation
disfavoured by a factor of ~ 600
Distribution is symmetric with peaks
at A=95 and A=140

## Slide 12
Assume fission from a nucleus at rest
Conservation of momentum
Conservation of Energy
So when the fission has a heavy fragment and a lighter fragment it is the lighter fragment that takes most of the kinetic energy
(16.3)

## Slide 13
NEUTRON EMISSION
On average 2.1 neutrons are emitted in Th fission, 2.5 in U fission and 2.9 in Pu fission
  Values increase by 0.05 per MeV as Tn of the neutron increases
Most of these are PROMPT neutrons emitted at the moment of fission
Some DELAYED neutrons (0.65% for 235U) are emitted following the b- decay of the fission product
  THESE ARE VERY IMPORTANT FOR REACTOR CONTROL
e.g. For 87Br 2% of the b- decays populate a state in 87Kr which is so highly excited (~8 MeV) that neutron emission is a likely decay mode
  Only appears after the b- decay with an apparent half life T1/2 = 54.5s

## Slide 14: Some examples of delayed neutrons
FISSION NEUTRON ENERGY SPECTRUM