## Slide 1: NEUTRON DIFFUSION
THE CONTINUITY EQUATION
Consider the number of neutrons in an infinitesimal volume dV
Loss of neutrons in x direction per second
Leakage = loss from entire volume
 FLUX LEAKAGE = - D  2F (21.1)

## Slide 2
NEUTRON DIFFUSION EQUATION
Introduce a source of neutrons
  S created per unit volume per second
  Allow for loss by absorption as well as by leakage
Rate of change of neutron density is
(21.2)
NEUTRON DIFFUSION EQUATION
For a STEADY STATE (21.3)
BOUNDARY CONDITIONS
F  0 and finite
F  same symmetry as reactor geometry
J and F continuous at interfaces between media
F  0 at boundary

## Slide 3
DIFFUSION LENGTH
If there are no sources and there is a steady state we have:-
                (21.4)
where L is the DIFFUSION LENGTH
The above equation is valid when there are LOCALISED
sources S which emit neutrons isotropically in an infinite medium
i.e. it applies in the spaces between the localised sources
If we have SPHERICAL SYMMETRY then
F(r,q,f)  F(r) only and

## Slide 4
The solution which satisfies the boundary conditions is
F(r)= (A/r) x exp(-r/L)
where A = constant
  Check the solution by substitution
The rate of absorption in the infinite volume is given

## Slide 5
CROW FLIGHT DISTANCE
Real neutrons are continually scattered so their path is a “RANDOM WALK”
The mean square ‘Crow Flight’ distance travelled from source S to absorption is
i.e. the actual distance travelled is related to the diffusion length
(21.5)

## Slide 6: THE REACTOR EQUATION
THERMAL NEUTRON VELOCITY DISTRIBUTION
Neutrons that are not being strongly absorbed reach thermal equilibrium with the medium in which they scatter i.e. the moderator
  Speeds have a Maxwell-Boltzmann distribution
n(v)dv is the number of neutrons / m3 with speeds between v and v+dv and T is the moderator temperature
INTEGRATION OF THE DIFFUSION EQUATION
We need to integrate
over the thermal neutron energy range Tn~ kT

## Slide 7
ASSUME
n(r, Tn, t) and F (r, Tn, t) are separable functions of r, Tn and t and use AVERAGE QUANTITIES I.E.
Now Sth(r,t) = rate of production of neutrons in core
= rate of production x rate of absorption
rate of absorption

## Slide 8
Define BUCKLING PARAMETER B
( Called the Material Buckling)
For a CRITICAL REACTOR
This is the REACTOR EQUATION (for the steady state)
21.6
21.7
21.8

## Slide 9
It is usual to write the relation for B2 as
B2 = (k∞ – 1)/LC2 where LC is neutron diffusion length in the core of the reactor
If the core is regarded as fuel + moderator only then
SA(C) = SA(F) + SA(M)
If LM is the diffusion length in the moderator we can express LC in terms of LM and the thermal utilisation factor f
f = SA(F) / [SA(F) + SA(M)] in this case and so
(1-f) = SA(M) / [SA(F) + SA(M)] = SA(M) / SA(C)
Since LC2 = D / SA(C) and LM2 = D / SA(M) we obtain
LC2 = (1 – f) LM2 (21.9)
(N.B. This is equivalent to using SA(C) in the formula for B (and L) on the previous slide.
To evaluate SA(C) and f you would need to know the relative composition of the core).

## Slide 10: Calculate the multiplication factor k∞ of a reactor core containing a mixture of uranium, enriched to 1.7% in 235U, and graphite with a ratio NGraphite : NU of 500:1 graphite atoms to fuel atoms given that the resonance escape probability p = 0.73 and the fast fission factor e = 1.02. 235U has sf (235) = 579 b , sA (235) = 680 b and density r = 18700 kg m-3, 238 U has sA (238) = 2.7 b and density r = 18700 kg m-3, Graphite has sA (graphite) = 0.0045 b and density r = 1600 kg m-3
First calculate f:
f = SA (fuel) /[SA (fuel) + SA (graphite)]
SA (fuel) = n235 sA (235) + n238 sA (238)
= NU (0.017 x sA (235) + 0.983 x sA (238)) = NU x 14.2 b
SA (graphite)] = NGraphite sA (graphite) = 500 NU sA (graphite)
= 500 NU x 0.0045 = NU x 2.25 b
So f = 14.2 / (14.2 + 2.25) = 0.863

## Slide 11
Now calculate h:
h= n x Sf (fuel) / SA (fuel)
Sf (fuel) = n235 sf (235) + n238 sf (238)
= NU (0.017 x sf (235) + 0.983 x 0.0) = NU x 9.84 b
SA (fuel) = NU x 14.2 b
h= 2.5 x 9.84 / 14.2 = 1.73
k∞ = e p f h = 1. x 0.73 x 0.863 x 1.73 = 1.11