Revisions required on hybrid

Number chips for simpler reference when scanning under scope

Put copper in tab area to stiffen it

Shrinkage of circuit is 0.25%  over 90mm detector 120mm fanout

This gives 225 and 300um difference in fanout size

This can be compensated by PCB people

Check fanout actual size…..